## Slide 1: DeNovo: A Software-Driven Rethinking of the Memory Hierarchy
Sarita Adve, Vikram Adve,
Rob Bocchino, Nicholas Carter, Byn Choi, Ching-Tsun Chou,
Stephen Heumann, Nima Honarmand, Rakesh Komuravelli, Maria Kotsifakou,
Tatiana Schpeisman, Matthew Sinclair, Robert Smolinski,
Prakalp Srivastava, Hyojin Sung, Adam Welc
University of Illinois at Urbana-Champaign, Intel
denovo@cs.illinois.edu

## Slide 2: Silver Bullets for the Energy Crisis?
Parallelism
Specialization, heterogeneity, …
BUT large impact on
  Software
  Hardware
  Hardware-Software Interface

## Slide 3: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software

## Slide 4: Specialization/Heterogeneity: Current Practice
6 different ISAs
7 different parallelism models
Incompatible
memory systems
A modern smartphone
    CPU, GPU, DSP, Vector Units, Multimedia, Audio-Video accelerators
Even more broken

## Slide 5: Energy Crisis Demands Rethinking HW, SW
How to (co-)design
  Software?
  Hardware?
  HW / SW Interface?
Deterministic Parallel Java (DPJ)
DeNovo
Virtual Instruction Set Computing (VISC)
Today: Focus on homogeneous parallelism

## Slide 6: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software

## Slide 7: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software
Banish shared memory?

## Slide 8: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complex, power- and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software
Banish wild shared memory!
Need disciplined shared memory!

## Slide 9: What is Shared-Memory?
Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 10: What is Shared-Memory?
Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 11: What is Shared-Memory?
Wild Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 12: What is Shared-Memory?
Wild Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization

## Slide 13: What is Shared-Memory?
Disciplined Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization
Explicit, structured side-effects
How to build disciplined shared-memory software?
If software is more disciplined, can hardware be more efficient?

## Slide 14: Our Approach
Simple programming model AND efficient hardware
Disciplined Shared Memory
Deterministic Parallel Java (DPJ): Strong safety properties
No data races, determinism-by-default, safe non-determinism
Simple semantics, safety, and composability
DeNovo: Complexity-, performance-, power-efficiency
Simplify coherence and consistency
Optimize communication and data storage
explicit effects +
structured
parallel control

## Slide 15: Key Milestones
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
Legacy, OS
Hardware
DeNovo
Coherence, Consistency,
Communication
    PACT’11 best paper
DeNovoND
ASPLOS’13 &
IEEE Micro top picks’14
DeNovoSynch (in review)
Ongoing
A language-oblivious virtual ISA
+ Storage

## Slide 16: Current Hardware Limitations
Complexity
  Subtle races and numerous transient states in the protocol
  Hard to verify and extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Bandwidth waste (cache-line based communication)
  Cache pollution (cache-line based allocation)

## Slide 17: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Bandwidth waste (cache-line based communication)
  Cache pollution (cache-line based allocation)
Base DeNovo
20X faster to verify vs. MESI

## Slide 18: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  No storage overhead for directory information
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Bandwidth waste (cache-line based communication)
  Cache pollution (cache-line based allocation)
Base DeNovo
20X faster to verify vs. MESI

## Slide 19: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  No storage overhead for directory information
Performance and power inefficiencies
  No invalidation, ack messages
  No indirection through directory
  No false sharing: region based coherence
  Region, not cache-line, communication
  Region, not cache-line, allocation (ongoing)
Up to 77% lower memory stall time
Up to 71% lower traffic
Base DeNovo
20X faster to verify vs. MESI

## Slide 20: DPJ Overview
Structured parallel control
  Fork-join parallelism
Region: name for set of memory locations
  Assign region to each field, array cell
Effect: read or write on a region
  Summarize effects of method bodies
Compiler: simple type check
  Region types consistent
  Effect summaries correct
  Parallel tasks don’t interfere (race-free)
heap
ST
ST
ST
ST
LD
Type-checked programs guaranteed determinism (sequential semantics)

## Slide 21: Memory Consistency Model
Guaranteed determinism  Read returns value of last write in sequential order
  Same task in this parallel phase
  Or before this parallel phase
LD 0xa
ST 0xa
Parallel
Phase
ST 0xa
Coherence
Mechanism

## Slide 22: Cache Coherence
Coherence Enforcement
  Invalidate stale copies in caches
  Track one up-to-date copy
Explicit effects
  Compiler knows all writeable regions in this parallel phase
  Cache can self-invalidate before next parallel phase
    Invalidates data in writeable regions not accessed by itself
Registration
  Directory keeps track of one up-to-date copy
  Writer updates before next parallel phase

## Slide 23: Basic DeNovo Coherence [PACT’11]
Assume (for now): Private L1, shared L2; single word line
  Data-race freedom at word granularity
No transient states
No invalidation traffic, no false sharing
No directory storage overhead
  L2 data arrays double as directory
  Keep valid data or registered core id
Touched bit: set if word read in the phase
registry
Invalid
Valid
Registered
Read
Write
Write
Read, Write
Read

## Slide 24: Example Run
R | X0 | V | Y0
R | X1 | V | Y1
R | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
class S_type {
X in DeNovo-region ;
Y in DeNovo-region ;
}
S _type S[size];
...
Phase1 writes { // DeNovo effect
foreach i in 0, size {
S[i].X = …;
}
self_invalidate( );
}
L1 of Core 1
R | X0 | V | Y0
R | X1 | V | Y1
R | X2 | V | Y2
I | X3 | V | Y3
I | X4 | V | Y4
I | X5 | V | Y5
L1 of Core 2
I | X0 | V | Y0
I | X1 | V | Y1
I | X2 | V | Y2
R | X3 | V | Y3
R | X4 | V | Y4
R | X5 | V | Y5
Shared L2
R | C1 | V | Y0
R | C1 | V | Y1
R | C1 | V | Y2
R | C2 | V | Y3
R | C2 | V | Y4
R | C2 | V | Y5
R = Registered
V = Valid
I = Invalid
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
R | X3 | V | Y3
R | X4 | V | Y4
R | X5 | V | Y5
Registration
Registration
Ack
Ack

## Slide 25: Decoupling Coherence and Tag Granularity
Basic protocol has tag per word
DeNovo Line-based protocol
  Allocation/Transfer granularity > Coherence granularity
    Allocate, transfer cache line at a time
    Coherence granularity still at word
    No word-level false-sharing
“Line Merging”
Cache
 |  | V |  |  | V | R | 
Tag
V | V |  |  |  |  |  | V

## Slide 26: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists (makes up for new bits at ~20 cores)
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Traffic (cache-line based communication)
  Cache pollution (cache-line based allocation)
✔
✔
✔
✔

## Slide 27: Flexible, Direct Communication
Insights
  1. Traditional directory must be updated at every transfer
  DeNovo can copy valid data around freely
  2. Traditional systems send cache line at a time
  DeNovo uses regions to transfer only relevant data
  Effect of AoS-to-SoA transformation w/o programmer/compiler

## Slide 28: Flexible, Direct Communication
L1 of Core 1
…
…
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
I | X3 | V | Y3 | V | Z3
I | X4 | V | Y4 | V | Z4
I | X5 | V | Y5 | V | Z5
L1 of Core 2
…
…
I | X0 | V | Y0 | V | Z0
I | X1 | V | Y1 | V | Z1
I | X2 | V | Y2 | V | Z2
R | X3 | V | Y3 | V | Z3
R | X4 | V | Y4 | V | Z4
R | X5 | V | Y5 | V | Z5
Shared L2
…
…
R | C1 | V | Y0 | V | Z0
R | C1 | V | Y1 | V | Z1
R | C1 | V | Y2 | V | Z2
R | C2 | V | Y3 | V | Z3
R | C2 | V | Y4 | V | Z4
R | C2 | V | Y5 | V | Z5
Registered
Valid
Invalid
X3
LD X3
Y3
Z3

## Slide 29: Flexible, Direct Communication
L1 of Core 1
…
…
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
I | X3 | V | Y3 | V | Z3
I | X4 | V | Y4 | V | Z4
I | X5 | V | Y5 | V | Z5
L1 of Core 2
…
…
I | X0 | V | Y0 | V | Z0
I | X1 | V | Y1 | V | Z1
I | X2 | V | Y2 | V | Z2
R | X3 | V | Y3 | V | Z3
R | X4 | V | Y4 | V | Z4
R | X5 | V | Y5 | V | Z5
Shared L2
…
…
R | C1 | V | Y0 | V | Z0
R | C1 | V | Y1 | V | Z1
R | C1 | V | Y2 | V | Z2
R | C2 | V | Y3 | V | Z3
R | C2 | V | Y4 | V | Z4
R | C2 | V | Y5 | V | Z5
Registered
Valid
Invalid
X3
X4
X5
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
V | X3 | V | Y3 | V | Z3
V | X4 | V | Y4 | V | Z4
V | X5 | V | Y5 | V | Z5
LD X3
Flexible, Direct Communication

## Slide 30: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists (makes up for new bits at ~20 cores)
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Traffic (cache-line based communication)
  Cache pollution (cache-line based allocation)
✔
✔
✔
✔
✔
✔
✔
Stash=cache+scratchpad,
another talk

## Slide 31: Evaluation
Verification: DeNovo vs. MESI word with Murphi model checker
  Correctness
    Six bugs in MESI protocol: Difficult to find and fix
    Three bugs in DeNovo protocol: Simple to fix
  Complexity
    15x fewer reachable states for DeNovo
    20x difference in the runtime
Performance: Simics + GEMS + Garnet
  64 cores, simple in-order core model
  Workloads
    FFT, LU, Barnes-Hut, and radix from SPLASH-2
    bodytrack and fluidanimate from PARSEC 2.1
    kd-Tree (two versions) [HPG 09]

## Slide 32
DeNovo is comparable to or better than MESI
DeNovo + opts shows 32% lower memory stalls vs. MESI (max 77%)
Memory Stall Time for MESI vs. DeNovo
Chart: 
| M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt
L2 Hit | 50.1646 | 33.7706 | 20.956 | 55.1987 | 42.0692 | 42.6177 | 80.8616 | 85.2234 | 76.7406 | 74.5951 | 25.286 | 22.7224 | 90.3029 | 90.4115 | 72.6525 | 97.4399 | 94.6733 | 93.656 | 83.2462 | 81.6431 | 78.3093 | 53.8131 | 56.4188 | 55.9461
R L1 Hit | 49.4678 | 61.468 | 20.2176 | 44.7923 | 2.5009 | 0.49821 | 19.1384 | 19.4893 | 6.683 | 25.167 | 0.88559 | 0.098262 | 9.2869 | 1.7655 | 0.2296 | 1.6829 | 2.5275 | 1.4248 | 7.4767 | 4.3489 | 1.3949 | 6.1086 | 7.7559 | 4.3095
Mem Hit | 0.36761 | 0.46032 | 0.46911 | 0.0090392 | 0.0076086 | 0.0078428 | 0 | 0 | 0 | 0.23794 | 0.25593 | 0.2554 | 0.41023 | 0.42994 | 0.35077 | 0.87722 | 0.9594 | 0.96951 | 9.2771 | 9.589 | 8.622 | 40.0783 | 36.5129 | 36.7414
FFT
LU
Barnes-Hut
kd-false
kd-padded
bodytrack
fluidanimate
radix
M=MESI D=DeNovo Dopt=DeNovo+Opt
Notes: Execution time average is 17%, max is 60%

## Slide 33
DeNovo has 36% less traffic than MESI (max 71%)
Network Traffic for MESI vs. DeNovo
Chart: 
| M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt
Read | 62.7927 | 39.4633 | 20.3722 | 55.1901 | 34.1295 | 34.2773 | 71.1048 | 70.6886 | 60.8695 | 67.7616 | 47.6313 | 42.4113 | 75.4643 | 74.4308 | 59.5776 | 79.0789 | 79.2869 | 81.2718 | 39.6484 | 37.2464 | 37.0966 | 48.9604 | 41.1327 | 41.1763
Write | 16.2984 | 5.9373 | 5.8867 | 12.3834 | 4.6144 | 4.9015 | 8.3643 | 5.3262 | 5.3059 | 13.0285 | 1.0009 | 0.99833 | 4.8158 | 1.4434 | 1.4497 | 3.948 | 1.2677 | 1.3364 | 22.7472 | 9.6064 | 9.8028 | 21.039 | 34.7101 | 34.9063
WB | 3.3653 | 2.2857 | 2.2438 | 16.5494 | 10.9907 | 11.6511 | 3.3206 | 5.011 | 5.0236 | 2.2534 | 1.132 | 1.2013 | 3.4753 | 1.7724 | 1.9186 | 2.7542 | 2.3585 | 2.4831 | 26.1851 | 22.4744 | 22.7333 | 19.271 | 22.8605 | 23.0132
Invalidation | 17.5436 | 0 | 0 | 15.8771 | 0 | 0 | 17.2102 | 0 | 0 | 16.9565 | 0 | 0 | 16.2445 | 0 | 0 | 14.219 | 0 | 0 | 11.4192 | 0 | 0 | 10.7296 | 0 | 0
FFT
LU
Barnes-Hut
kd-false
kd-padded
bodytrack
fluidanimate
radix
M=MESI D=DeNovo Dopt=DeNovo+Opt

## Slide 34: Key Milestones
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
Legacy, OS
Hardware
DeNovo
Coherence, Consistency,
Communication
    PACT’11 best paper
DeNovoND
ASPLOS’13 &
IEEE Micro top picks’14
DeNovoSynch (in review)
Ongoing
A language-oblivious virtual ISA
+ Storage

## Slide 35: DPJ Support for Disciplined Non-Determinism
Non-determinism comes from conflicting concurrent accesses
Isolate interfering accesses as atomic
  Enclosed in atomic sections
  Atomic regions and effects
Disciplined non-determinism
  Race freedom, strong isolation
  Determinism-by-default semantics
DeNovoND converts atomic statements into locks
.
.
.
.
.
.
ST
LD

## Slide 36: Memory Consistency Model
.
.
.
.
.
Non-deterministic read returns value of last write from
  Before this parallel phase
  Or same task in this phase
  Or in preceding critical section of same lock
LD 0xa
ST 0xa
ST 0xa
Critical
Section
Parallel
Phase
self-invalidations as before
single core

## Slide 37: Coherence for Non-Deterministic Data
When to invalidate?
  Between start of critical section and read
What to invalidate?
  Entire cache? Regions with “atomic” effects?
  Track atomic writes in a signature, transfer with lock
Registration
  Writer updates before next critical section
Coherence Enforcement
  Invalidate stale copies in private cache
  Track up-to-date copy

## Slide 38: Tracking Data Write Signatures
Small Bloom filter per core tracks writes signature
  Only track atomic effects
  Only 256 bits suffice
Operations on Bloom filter
  On write: insert address
  On read: query filter for address for self-invalidation

## Slide 39: Distributed Queue-based Locks
Lock primitive that works on DeNovoND
  No sharers-list, no write invalidation  No spinning for lock
Modeled after QOSB Lock [Goodman et al. ‘89]
  Lock requests form a distributed queue
  But much simpler
Details in ASPLOS’13

## Slide 40: Example Run
lock transfer
V | X | R | Y
V | Z | V | W
V | X | R | Y
I | Z | V | W
V | X | R | Y
V | Z | V | W
R | X | V | Y
V | Z | V | W
R | X | V | Y
R | Z | V | W
R | C1 | R | C2
V | Z | V | W
R | C1 | R | C2
R | C1 | V | W
lock transfer
ST
LD
ST
.
.
self-invalidate( )
L1 of Core 1
L1 of Core 2
Shared L2
Z W
Registration
Ack
Read miss
X in DeNovo-region
Y in DeNovo-region
Z in atomic DeNovo-region
W in atomic DeNovo-region
LD
V | X | R | Y
V | Z | R | W
R | X | V | Y
R | Z | I | W
Registration
R | C1 | R | C2
R | C1 | R | C2
Ack
Read miss
R | X | V | Y
R | Z | V | W
self-invalidate( )
reset filter
R | X | V | Y
R | Z | I | W
V | X | R | Y
I | Z | R | W
Z W

## Slide 41: Optimizations to Reduce Self-Invalidation
Loads in Registered state
Touched-atomic bit
  Set on first atomic load
  Subsequent loads don’t self-invalidate
.
.
X in DeNovo-region
Y in DeNovo-region
Z in atomic DeNovo-region
W in atomic DeNovo-region
ST
LD
self-invalidate( )
LD
LD

## Slide 42: Overheads
Hardware Bloom filter
  256 bits per core
Storage overhead
  One additional state, but no storage overhead (2 bits)
  Touched-atomic bit per word in L1
Communication overhead
  Bloom filter piggybacked on lock transfer message
  Writeback messages for locks
    Lock writebacks carry more info

## Slide 43: Evaluation of MESI vs. DeNovoND (16 cores)
DeNovoND execution time comparable or better than MESI
DeNovoND has 33% less traffic than MESI (67% max)
  No invalidation traffic
  Reduced load misses due to lack of false sharing

## Slide 44: Key Milestones
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
Legacy, OS
Hardware
DeNovo
Coherence, Consistency,
Communication
    PACT’11 best paper
DeNovoND
ASPLOS’13 &
IEEE Micro top picks’14
DeNovoSynch (in review)
Ongoing
A language-oblivious virtual ISA
+ Storage

## Slide 45: Unstructured Synchronization
Many programs (libraries) use unstructured synchronization
  E.g., non-blocking, wait-free constructs
  Arbitrary synchronization races
  Several reads and writes
Data ordered by such synchronization may still be disciplined
  Use static or signature driven self-invalidations
But what about synchronization accesses?

## Slide 46: Unstructured Synchronization
Memory model: Sequential consistency
What to invalidate, when to invalidate?
  Every read?
  Every read to non-registered state
  Register read (to enable future hits)
Concurrent readers?
  Back off (delay) read registration

## Slide 47: Unstructured Synch: Execution Time (64 cores)
DeNovoSync reduces execution time by 28% over MESI (max 49%)

## Slide 48: Unstructured Synch: Network Traffic (64 cores)
DeNovo reduces traffic by 44% vs. MESI (max 61%) for 11 of 12 cases
Centralized barrier
  Many concurrent readers hurt DeNovo (and MESI)
  Should use tree barrier even with MESI

## Slide 49: Key Milestones
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
Legacy, OS
Hardware
DeNovo
Coherence, Consistency,
Communication
    PACT’11 best paper
DeNovoND
ASPLOS’13 &
IEEE Micro top picks’14
DeNovoSynch (in review)
Ongoing
A language-oblivious virtual ISA
+ Storage

## Slide 50: Conclusions and Future Work (1 of 3)
Simple programming model AND efficient hardware
Disciplined Shared Memory
Deterministic Parallel Java (DPJ): Strong safety properties
No data races, determinism-by-default, safe non-determinism
Simple semantics, safety, and composability
DeNovo: Complexity-, performance-, power-efficiency
Simplify coherence and consistency
Optimize communication and storage
explicit effects +
structured
parallel control

## Slide 51: Conclusions and Future Work (2 of 2)
DeNovo rethinks hardware for disciplined models
For deterministic codes
Complexity
  No transient states: 20X faster to verify than MESI
  Extensible: optimizations without new states
Storage overhead
  No directory overhead
Performance and power inefficiencies
  No invalidations, acks, false sharing, indirection
  Flexible, not cache-line, communication
  Up to 77% lower memory stall time, up to 71% lower traffic
Added safe non-determinism and unstructured synchs

## Slide 52: Conclusions and Future Work (3 of 3)
Broaden software supported
  OS, legacy, …
Region-driven memory hierarchy
  Also apply to heterogeneous memory
    Global address space
    Region-driven coherence, communication, layout
    Stash = best of cache and scratchpad
Hardware/Software Interface
  Language-neutral virtual ISA
Parallelism and specialization may solve energy crisis, but
  Require rethinking software, hardware, interface