## Slide 1: DeNovo: A Software-Driven Rethinking of the Memory Hierarchy
Sarita Adve
with
Vikram Adve, Rob Bocchino, Nicholas Carter, Byn Choi,
Ching-Tsun Chou, Stephen Heumann, Nima Honarmand,
Rakesh Komuravelli, Maria Kotsifakou,
Tatiana Schpeisman, Matthew Sinclair, Robert Smolinski,
Prakalp Srivastava, Hyojin Sung, Adam Welc
University of Illinois, Intel, EPFL
denovo@cs.illinois.edu
sarita.adve@epfl.ch

## Slide 2: Silver Bullets for the Energy Crisis?
Parallelism
Specialization, heterogeneity, …
BUT large impact on
  Software
  Hardware
  Hardware-Software Interface

## Slide 3: Multicore Parallelism: Current Practice
Multicore parallelism today: shared-memory
  Complexity-, power-, and performance-inefficient hardware
    Complex directory coherence, unnecessary traffic, ...
  Difficult programming model
    Data races, non-determinism, composability?, testing?
  Mismatched interface between HW and SW, a.k.a memory model
    Can’t specify “what value can read return”
    Data races defy acceptable semantics
Fundamentally broken for hardware & software

## Slide 4: Specialization/Heterogeneity: Current Practice
6 different ISAs
7 different parallelism models
Incompatible
memory systems
A modern smartphone
    CPU, GPU, DSP, Vector Units, Multimedia, Audio-Video accelerators
Even more broken

## Slide 5: Energy Crisis Demands Rethinking HW, SW
How to (co-)design
  Software?
  Hardware?
  HW / SW Interface?
Deterministic Parallel Java (DPJ)
DeNovo
Virtual Instruction Set Computing (VISC)
Other implications of energy crisis (another talk)
  SWAT: SoftWare Anomaly Treatment
    A software-driven approach to hardware reliability

## Slide 6: Memory Hierarchy Inefficiencies
Complex protocols
Directory storage
Traffic: Invalidation, Acks, …
Cache lines  false sharing
Caches: SW-oblivious
  Power: TLB/Tags
  Cache lines sub-optimal
Scratchpads, FIFOs, …
  Explicit data movement
Indirection through directory
Cache lines sub-optimal
Coherence & Consistency
Storage
Communication
Complexity-, power-, and performance-inefficient hardware

## Slide 7: Memory Hierarchy Inefficiencies
Complex protocols
Directory storage
Traffic: Invalidation, Acks, …
Cache lines  false sharing
Caches: SW-oblivious
  Power: TLB/Tags
  Cache lines sub-optimal
Scratchpads, FIFOs, …
  Explicit data movement
Indirection through directory
Cache lines sub-optimal
Coherence & Consistency
Storage
Communication
Complexity-, power-, and performance-inefficient hardware
Banish shared memory?

## Slide 8: Memory Hierarchy Inefficiencies
Complex protocols
Directory storage
Traffic: Invalidation, Acks, …
Cache lines  false sharing
Caches: SW-oblivious
  Power: TLB/Tags
  Cache lines sub-optimal
Scratchpads, FIFOs, …
  Explicit data movement
Indirection through directory
Cache lines sub-optimal
Coherence & Consistency
Storage
Communication
Complexity-, power-, and performance-inefficient hardware
Banish wild shared memory!
Need disciplined shared memory!

## Slide 9: What is Shared-Memory?
Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization
Coherence
Storage
Comm

## Slide 10: What is Shared-Memory?
Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization
Coherence
Storage
Comm

## Slide 11: What is Shared-Memory?
Wild Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization
Coherence
Storage
Comm

## Slide 12: What is Shared-Memory?
Wild Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization
Coherence
Storage
Comm

## Slide 13: What is Shared-Memory?
Disciplined Shared-Memory =
Global address space
+
Implicit, anywhere communication, synchronization
Explicit, structured side-effects
How to build disciplined shared-memory software?
If software is more disciplined, can hardware be more efficient?
Coherence
Storage
Comm

## Slide 14: The DeNovo Approach
Hardware
DeNovo: Coherence, Comm
PACT’11 best paper, TACO’14
DeNovoND
ASPLOS’13, Top picks’14
DeNovoSync (in review)
Coherence
Storage
Comm
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
 OS, Legacy
DeNovoH for heterogeneous systems: Coherence, Comm, Storage
Stash: Have your scratchpad and cache it too (in review)

## Slide 15: Coherence/Communication Inefficiencies
Complexity
  Subtle races and numerous transient states in the protocol
  Hard to verify and extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Network traffic (cache-line based communication)

## Slide 16: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  Directory overhead for sharer lists
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Network traffic (cache-line based communication)
Base DeNovo
20X faster to verify vs. MESI

## Slide 17: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  No storage overhead for directory information
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Network traffic (cache-line based communication)
Base DeNovo
20X faster to verify vs. MESI

## Slide 18: Results for Deterministic Codes
Complexity
  No transient states
  Simple to extend for optimizations
Storage overhead
  No storage overhead for directory information
Performance and power inefficiencies
  No invalidation, ack messages
  No indirection through directory
  No false sharing: region based coherence
Up to 77% lower memory stall time
Up to 71% lower traffic
Base DeNovo
20X faster to verify vs. MESI

## Slide 19: Deterministic Parallel Java (DPJ) Overview
Structured parallel control
  Fork-join parallelism
Region: name for set of memory locations
  Assign region to each field, array cell
Effect: read or write on a region
  Summarize effects of method bodies
Compiler: simple type check
  Region types consistent
  Effect summaries correct
  Parallel tasks don’t interfere (race-free)
heap
ST
ST
ST
ST
LD
Type-checked programs guaranteed determinism (sequential semantics)

## Slide 20: Memory Consistency Model
Guaranteed determinism  Read returns value of last write in sequential order
  Same task in this parallel phase
  Or before this parallel phase
LD 0xa
ST 0xa
Parallel
Phase
ST 0xa
Coherence
Mechanism

## Slide 21: Cache Coherence
Coherence Enforcement
  Invalidate stale copies in caches
  Track one up-to-date copy
Explicit effects
  Compiler knows all writeable regions in this parallel phase
  Cache can self-invalidate before next parallel phase
    Invalidates data in writeable regions not accessed by itself
Registration
  Directory keeps track of one up-to-date copy
  Writer updates before next parallel phase

## Slide 22: Basic DeNovo Coherence [PACT’11]
Assume (for now): Private L1, shared L2; single word line
  Data-race freedom at word granularity
No transient states
No invalidation traffic, no false sharing
No directory storage overhead
  L2 data arrays double as directory
  Keep valid data or registered core id
Touched bit: set if word read in the phase
registry
Invalid
Valid
Registered
Read
Write
Write
Read, Write
Read

## Slide 23: Example Run
R | X0 | V | Y0
R | X1 | V | Y1
R | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
class S_type {
X in DeNovo-region ;
Y in DeNovo-region ;
}
S _type S[size];
...
Phase1 writes { // DeNovo effect
foreach i in 0, size {
S[i].X = …;
}
self_invalidate( );
}
L1 of Core 1
R | X0 | V | Y0
R | X1 | V | Y1
R | X2 | V | Y2
I | X3 | V | Y3
I | X4 | V | Y4
I | X5 | V | Y5
L1 of Core 2
I | X0 | V | Y0
I | X1 | V | Y1
I | X2 | V | Y2
R | X3 | V | Y3
R | X4 | V | Y4
R | X5 | V | Y5
Shared L2
R | C1 | V | Y0
R | C1 | V | Y1
R | C1 | V | Y2
R | C2 | V | Y3
R | C2 | V | Y4
R | C2 | V | Y5
R = Registered
V = Valid
I = Invalid
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
V | X3 | V | Y3
V | X4 | V | Y4
V | X5 | V | Y5
V | X0 | V | Y0
V | X1 | V | Y1
V | X2 | V | Y2
R | X3 | V | Y3
R | X4 | V | Y4
R | X5 | V | Y5
Registration
Registration
Ack
Ack

## Slide 24: Decoupling Coherence and Tag Granularity
Basic protocol has tag per word
DeNovo Line-based protocol
  Allocation/Transfer granularity > Coherence granularity
    Allocate, transfer cache line at a time
    Coherence granularity still at word
    No word-level false-sharing
“Line Merging”
Cache
 |  | V |  |  | V | R | 
Tag
V | V |  |  |  |  |  | V

## Slide 25: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists (makes up for new bits at ~20 cores)
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Network traffic (cache-line based communication)
✔
✔
✔
✔

## Slide 26: Flexible, Direct Communication
Insights
  1. Traditional directory must be updated at every transfer
  DeNovo can copy valid data around freely
  2. Traditional systems send cache line at a time
  DeNovo uses regions to transfer only relevant data
  Effect of AoS-to-SoA transformation w/o programmer/compiler

## Slide 27: Flexible, Direct Communication
L1 of Core 1
…
…
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
I | X3 | V | Y3 | V | Z3
I | X4 | V | Y4 | V | Z4
I | X5 | V | Y5 | V | Z5
L1 of Core 2
…
…
I | X0 | V | Y0 | V | Z0
I | X1 | V | Y1 | V | Z1
I | X2 | V | Y2 | V | Z2
R | X3 | V | Y3 | V | Z3
R | X4 | V | Y4 | V | Z4
R | X5 | V | Y5 | V | Z5
Shared L2
…
…
R | C1 | V | Y0 | V | Z0
R | C1 | V | Y1 | V | Z1
R | C1 | V | Y2 | V | Z2
R | C2 | V | Y3 | V | Z3
R | C2 | V | Y4 | V | Z4
R | C2 | V | Y5 | V | Z5
Registered
Valid
Invalid
X3
LD X3
Y3
Z3

## Slide 28: Flexible, Direct Communication
L1 of Core 1
…
…
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
I | X3 | V | Y3 | V | Z3
I | X4 | V | Y4 | V | Z4
I | X5 | V | Y5 | V | Z5
L1 of Core 2
…
…
I | X0 | V | Y0 | V | Z0
I | X1 | V | Y1 | V | Z1
I | X2 | V | Y2 | V | Z2
R | X3 | V | Y3 | V | Z3
R | X4 | V | Y4 | V | Z4
R | X5 | V | Y5 | V | Z5
Shared L2
…
…
R | C1 | V | Y0 | V | Z0
R | C1 | V | Y1 | V | Z1
R | C1 | V | Y2 | V | Z2
R | C2 | V | Y3 | V | Z3
R | C2 | V | Y4 | V | Z4
R | C2 | V | Y5 | V | Z5
Registered
Valid
Invalid
X3
X4
X5
R | X0 | V | Y0 | V | Z0
R | X1 | V | Y1 | V | Z1
R | X2 | V | Y2 | V | Z2
V | X3 | V | Y3 | V | Z3
V | X4 | V | Y4 | V | Z4
V | X5 | V | Y5 | V | Z5
LD X3
Flexible, Direct Communication

## Slide 29: Current Hardware Limitations
Complexity
  Subtle races and numerous transient sates in the protocol
  Hard to extend for optimizations
Storage overhead
  Directory overhead for sharer lists (makes up for new bits at ~20 cores)
Performance and power inefficiencies
  Invalidation, ack messages
  Indirection through directory
  False sharing (cache-line based coherence)
  Network traffic (cache-line based communication)
✔
✔
✔
✔
✔
✔
✔

## Slide 30: Evaluation
Verification: DeNovo vs. MESI word w/ Murphi model checker
  Correctness
    Six bugs in MESI protocol: Difficult to find and fix
    Three bugs in DeNovo protocol: Simple to fix
  Complexity
    15x fewer reachable states for DeNovo
    20x difference in the runtime
Performance: Simics + GEMS + Garnet
  64 cores, simple in-order core model
  Workloads
    FFT, LU, Barnes-Hut, and radix from SPLASH-2
    bodytrack and fluidanimate from PARSEC 2.1
    kd-Tree (two versions) [HPG 09]

## Slide 31
DeNovo is comparable to or better than MESI
DeNovo + opts shows 32% lower memory stalls vs. MESI (max 77%)
Memory Stall Time for MESI vs. DeNovo
Chart: 
| M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt
L2 Hit | 50.1646 | 33.7706 | 20.956 | 55.1987 | 42.0692 | 42.6177 | 80.8616 | 85.2234 | 76.7406 | 74.5951 | 25.286 | 22.7224 | 90.3029 | 90.4115 | 72.6525 | 97.4399 | 94.6733 | 93.656 | 83.2462 | 81.6431 | 78.3093 | 53.8131 | 56.4188 | 55.9461
R L1 Hit | 49.4678 | 61.468 | 20.2176 | 44.7923 | 2.5009 | 0.49821 | 19.1384 | 19.4893 | 6.683 | 25.167 | 0.88559 | 0.098262 | 9.2869 | 1.7655 | 0.2296 | 1.6829 | 2.5275 | 1.4248 | 7.4767 | 4.3489 | 1.3949 | 6.1086 | 7.7559 | 4.3095
Mem Hit | 0.36761 | 0.46032 | 0.46911 | 0.0090392 | 0.0076086 | 0.0078428 | 0 | 0 | 0 | 0.23794 | 0.25593 | 0.2554 | 0.41023 | 0.42994 | 0.35077 | 0.87722 | 0.9594 | 0.96951 | 9.2771 | 9.589 | 8.622 | 40.0783 | 36.5129 | 36.7414
FFT
LU
Barnes-Hut
kd-false
kd-padded
bodytrack
fluidanimate
radix
M=MESI D=DeNovo Dopt=DeNovo+Opt

## Slide 32
DeNovo has 36% less traffic than MESI (max 71%)
Network Traffic for MESI vs. DeNovo
Chart: 
| M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt | M | D | Dopt
Read | 62.7927 | 39.4633 | 20.3722 | 55.1901 | 34.1295 | 34.2773 | 71.1048 | 70.6886 | 60.8695 | 67.7616 | 47.6313 | 42.4113 | 75.4643 | 74.4308 | 59.5776 | 79.0789 | 79.2869 | 81.2718 | 39.6484 | 37.2464 | 37.0966 | 48.9604 | 41.1327 | 41.1763
Write | 16.2984 | 5.9373 | 5.8867 | 12.3834 | 4.6144 | 4.9015 | 8.3643 | 5.3262 | 5.3059 | 13.0285 | 1.0009 | 0.99833 | 4.8158 | 1.4434 | 1.4497 | 3.948 | 1.2677 | 1.3364 | 22.7472 | 9.6064 | 9.8028 | 21.039 | 34.7101 | 34.9063
WB | 3.3653 | 2.2857 | 2.2438 | 16.5494 | 10.9907 | 11.6511 | 3.3206 | 5.011 | 5.0236 | 2.2534 | 1.132 | 1.2013 | 3.4753 | 1.7724 | 1.9186 | 2.7542 | 2.3585 | 2.4831 | 26.1851 | 22.4744 | 22.7333 | 19.271 | 22.8605 | 23.0132
Invalidation | 17.5436 | 0 | 0 | 15.8771 | 0 | 0 | 17.2102 | 0 | 0 | 16.9565 | 0 | 0 | 16.2445 | 0 | 0 | 14.219 | 0 | 0 | 11.4192 | 0 | 0 | 10.7296 | 0 | 0
FFT
LU
Barnes-Hut
kd-false
kd-padded
bodytrack
fluidanimate
radix
M=MESI D=DeNovo Dopt=DeNovo+Opt

## Slide 33: The DeNovo Approach
Hardware
DeNovo: Coherence, Comm
PACT’11 best paper, TACO’14
DeNovoND
ASPLOS’13, Top picks’14
DeNovoSync (in review)
Coherence
Storage
Comm
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
 OS, Legacy
DeNovoH for heterogeneous systems: Coherence, Comm, Storage
Stash: Have your scratchpad and cache it too (in review)

## Slide 34: DPJ Support for Disciplined Non-Determinism
Non-determinism comes from conflicting concurrent accesses
Isolate interfering accesses as atomic
  Enclosed in atomic sections
  Atomic regions and effects
Disciplined non-determinism
  Race freedom, strong isolation
  Determinism-by-default semantics
DeNovoND converts atomic statements into locks
.
.
.
.
.
.
ST
LD

## Slide 35: Memory Consistency Model
.
.
.
.
.
Non-deterministic read returns value of last write from
  Before this parallel phase
  Or same task in this phase
  Or in preceding critical section of same lock
LD 0xa
ST 0xa
ST 0xa
Critical
Section
Parallel
Phase
self-invalidations as before
single core

## Slide 36: Coherence for Non-Deterministic Data
When to invalidate?
  Between start of critical section and read
What to invalidate?
  Regions with “atomic” effects written in preceding critical sections
  Track writes w/ small (256b) Bloom filter signature, Xfer with lock
Registration
  Writer updates registry before next critical section
Coherence Enforcement
  Invalidate stale copies in private cache
  Track up-to-date copy

## Slide 37: Evaluation of MESI vs. DeNovoND (16 cores)
DeNovoND execution time comparable or better than MESI
DeNovoND has 33% less traffic than MESI (67% max)
  No invalidation traffic
  Reduced load misses due to lack of false sharing

## Slide 38: The DeNovo Approach
Hardware
DeNovo: Coherence, Comm
PACT’11 best paper, TACO’14
DeNovoND
ASPLOS’13, Top picks’14
DeNovoSync (in review)
Coherence
Storage
Comm
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
 OS, Legacy
DeNovoH for heterogeneous systems: Coherence, Comm, Storage
Stash: Have your scratchpad and cache it too (in review)

## Slide 39: Unstructured Synchronization
void queue.enqueue(value v):
node *w := new node(v, null)
ptr t, n
loop
t := tail
n := t->next
if t == tail
if n == null
if (CAS(&t->next, n, w)) break;
else CAS(&tail, t, n)
CAS(&tail, t, w)
Accesses to data still ordered by synchronization (data-race-free)
  Can use static self-invalidation or signatures
But what about synchronization accesses?
Michael-Scott non-blocking queue
Synchronization
Reads to
tail and tail->next
New node
to be inserted
CAS to
tail and tail->next
Many programs use arbitrary, unstructured synchronization

## Slide 40: Unstructured Synchronization
Problem: Synchronization accesses are inherently racy
  Rely on writer-initiated invalidations
Reader-initiated invalidations
  What to invalidate, when to invalidate?
    Every read?
    Every read to non-registered state
    Register all sync reads (to enable future hits)
  Concurrent readers?
    Back off (delay) read registration
ST
CAS
ST
LD
LD
REL
CAS
LD
.
.
.
.
.
.

## Slide 41: Unstructured Synch: Execution Time on 64 Cores
DeNovoSync reduces execution time by 28% over MESI (max 49%)
    MESI’s high invalidation overhead vs.
    DeNovo’s fast point-to-point registration transfer

## Slide 42: Unstructured Synch: Network Traffic on 64 Cores
DeNovo reduces traffic by 44% vs. MESI (max 61%) for 11 of 12 cases
Centralized barrier
  Many concurrent readers hurt DeNovo (and MESI)
  Should use tree barrier even with MESI

## Slide 43: The DeNovo Approach
Hardware
DeNovo: Coherence, Comm
    PACT’11 best paper
DeNovoND
ASPLOS’13, Top picks’14
DeNovoSync (in review)
Coherence
Storage
Comm
Software
DPJ: Determinism
OOPSLA’09
Disciplined non-determinism
      POPL’11
Unstructured synchronization
 OS, Legacy
DeNovoH for heterogeneous systems: Coherence, Comm, Storage
Stash: Have your scratchpad and cache it too (in review)

## Slide 44: Conclusions and Future Work
DeNovo rethinks memory hierarchy
for disciplined models
For deterministic codes
  Complexity: no transients, 20X faster to verify, extensible
  Storage overhead: no directory overhead
  Performance, power: No inv/acks, false sharing, indirection, …
    Up to 77% lower memory stall time, up to 71% lower traffic
Benefits even for non-determinism and unstructured synchs
Future
  Run full OS, legacy codes
  Heterogeneous memory structures and consistency models
  Virtual ISA for heterogeneous systems
Coherence
Storage
Comm