## Slide 1: DeNovoSync: Efficient Support for Arbitrary Synchronization without Writer-Initiated Invalidations
Hyojin Sung and Sarita Adve
  Department of Computer Science
University of Illinois, EPFL

## Slide 2: Motivation
Shared Memory
Complex software
Data races, non-determinism, implicit communication, …
Complex, inefficient hardware
Complex coherence, consistency, unnecessary traffic, ...

## Slide 3: Motivation
WILD Shared Memory
Complex software
Data races, non-determinism, implicit communication, …
Complex, inefficient hardware
Complex coherence, consistency, unnecessary traffic, ...

## Slide 4: Motivation
WILD Shared Memory
Complex software
Data races, non-determinism, implicit communication, …
Complex, inefficient hardware
Complex coherence, consistency, unnecessary traffic, ...
Disciplined

## Slide 5: Motivation
Disciplined Shared Memory
Complex software
Data races, non-determinism, implicit communication, …
Complex, inefficient hardware
Complex coherence, consistency, unnecessary traffic, ...
Structured synch +
Explicit memory side effects

## Slide 6: Motivation
Disciplined Shared Memory
Complex software
No data races, safe non-determinism, explicit sharing, …
Complex, inefficient hardware
Complex coherence, consistency, unnecessary traffic, ...
Structured synch +
Explicit memory side effects
Simpler

## Slide 7: Motivation
Disciplined Shared Memory
Complex software
No data races, safe non-determinism, explicit sharing, …
Complex, inefficient hardware
Complex coherence, consistency, unnecessary traffic, ...
Structured synch +
Explicit memory side effects
Simpler

## Slide 8: Motivation
Complex software
No data races, safe non-determinism, explicit sharing, …
Complex, inefficient hardware
DeNovo [PACT11], DeNovoND [ASPLOS13, Top Picks 14]
Simpler
Simpler, more efficient
Disciplined Shared Memory
Structured synch +
Explicit memory side effects
BUT focus on data accesses, synchronization restricted
BUT much software (runtime, OS, …) uses unstructured synch

## Slide 9: Motivation
Complex software
No data races, safe non-determinism, explicit sharing, …
Complex, inefficient hardware
DeNovo [PACT11], DeNovoND [ASPLOS13, Top Picks 14]
Simpler
Simpler, more efficient
Disciplined Shared Memory
Structured synch +
Explicit memory side effects
BUT focus on data accesses, synchronization restricted
BUT much software (runtime, OS, …) uses unstructured synch
DeNovoSync:
Support arbitrary synchronization with advantages of DeNovo

## Slide 10: Supporting Arbitrary Synchronization: The Challenge
MESI: Writer sends invalidations to cached copies to avoid stale data
Prior DeNovo assumptions
  Race-freedom
  Restricted synchronization with special hardware
   Reader self-invalidates stale data
Cache 1
Cache 2
Read A
Write A
A
INV
 Directory storage, inv/ack msgs, transient states, …
A
BUT Synchronization?
Naïve: Don’t cache synch
Notes: So what’s the challenge? Conventional coherence protocols such as MESI rely on writer-initiated invalidations to all cached copies to remove stale data. This requires supporting a directory, extra messages, transient states, etc. leading to complexity and inefficiency.

## Slide 11: Contributions of DeNovoSync
DeNovoSync: Cache arbitrary synch w/o writer invalidations
Simplicity, perf, energy advantages of DeNovo w/o sw restrictions
DeNovoSync vs. MESI for 24 kernels (16 & 64 cores), 13 apps
  Kernels: 22% lower exec time, 58% lower traffic for 44 of 48 cases
  Apps: 4% lower exec time, 24% lower traffic for 12 of 13 cases

## Slide 12: Outline
Motivation
Background: DeNovo Coherence for Data
DeNovoSync Design
Experiments
Conclusions

## Slide 13: DeNovo Coherence for Data (1 of 2)
Original DeNovo software assumptions [PACT’11]
  Data-race-free
  Synchronization: Barriers demarcate parallel phases
  Writeable data regions in parallel phase are explicit
Coherence
  Read hit: Don’t return stale data
    Before next parallel phase, cache selectively self-invalidates
      Needn’t invalidate data it accessed in previous phase
  Read miss: Find one up-to-date copy
    Write miss registers at “directory”
    Shared LLC data arrays double as registry
      Keep valid data or registered core id
W
W
registry

## Slide 14: DeNovo Coherence for Data (2 of 2)
More complexity-, performance-, and energy-efficient than MESI
DeNovoND adds structured locks [ASPLOS’13, Top Picks’14]
  When to self-invalidate: at lock acquire
  What data to self-invalidate: dynamically collected modified data signatures
  Special hardware support for locks
Invalid
Valid
Registered
Read
Write
Write
Read, Write
Read
No transient states
No invalidation traffic
No directory storage overhead
No false sharing (word coherence)
But how to handle arbitrary synchronization?

## Slide 15: Outline
Motivation
Background: DeNovo Coherence for Data
DeNovoSync Design
Experiments
Conclusions

## Slide 16: Unstructured Synchronization
void queue.enqueue(value v):
node *w := new node(v, null)
ptr t, n
loop
t := tail
n := t->next
if t == tail
if n == null
if (CAS(&t->next, n, w)) break;
else CAS(&tail, t, n)
CAS(&tail, t, w)
Data accesses ordered by synchronization
  Self-invalidate at synch using static regions or dynamic signatures
But what about synchronization?
Michael-Scott non-blocking queue
New node
to be inserted

## Slide 17: DeNovoSync: Software Requirements
Software requirement: Data-race-free
  Distinguish synchronization vs. data accesses to hardware
  Obeyed by C++, C, Java, …
Semantics: Sequential consistency
Optional software information for data consistency performance

## Slide 18: DeNovoSync0 Protocol
Key: Synch read should not return stale data
When to self-invalidate synch location?
  Every synch read?
  Every synch read to non-registered state
DeNovoSync0 registers (serializes) synch reads
  Successive reads hit
  Updates propagate to readers
CAS
LD
ST
Core 1
Core 2
LD
ACQ
REL
LD
LD
Test&Test&Set Lock

## Slide 19: DeNovoSync0 Protocol
Key: Synch read should not return stale data
When to self-invalidate synch location?
  Every synch read?
  Every synch read to non-registered state
DeNovoSync0 registers (serializes) synch reads
  Successive reads hit
  Updates propagate to readers
  BUT many registration transfers for Read-Read races
CAS
LD
LD
ST
CAS
Core 1
Core 3
Core 2
LD
LD
LD
ACQ
ACQ
REL
LD
LD
LD
Test&Test&Set Lock

## Slide 20: DeNovoSync = DeNovoSync0 + Hardware Backoff
Hardware backoff to reduce Read-Read races
  Remote synch read requests = hint for contention
  Delay next (local) synch read miss for backoff cycles
Two-level adaptive counters for backoff cycles
  B = Per-core backoff counter
    On remote synch read request, B ← B + I
  I = Per-core increment counter
    D = Default increment value
    On Nth remote synch read request, I ← I + D
    N determined by system configuration
Read-Read races  Contention  Backoff!
More Read-Read races  More contention  Backoff longer!

## Slide 21: Example
LD
LD
ACQ
ACQ
REL
LD
LD
Thread 1
Thread 2
Thread 3
Core 1
Core 2
Core 3
Registered
Invalid
0
0
0
C1
HIT
Backoff
Shared Cache
ST
Test&Test&Set Lock
Invalid

## Slide 22: Example
LD
LD
ACQ
ACQ
REL
LD
LD
Thread 1
Thread 2
Thread 3
Core 1
Core 2
Core 3
Registered
0
0
0
C1
C2
Valid
16
Backoff
Shared Cache
BACKOFF
ST
Test&Test&Set Lock
Invalid
Registered

## Slide 23: Example
C2
LD
ST
ACQ
ACQ
REL
LD
LD
CAS
LD
Thread 1
Thread 2
Thread 3
Core 1
Core 2
Core 3
Registered
16
0
0
Valid
Registered
C3
Invalid
Shared Cache
Backoff
C3
LD

## Slide 24: Example
C2
LD
ST
ACQ
ACQ
REL
LD
LD
CAS
LD
Thread 1
Thread 2
Thread 3
Core 1
Core 2
Core 3
16
0
0
Valid
Invalid
C3
Registered
Shared Cache
Backoff
C2
LD

## Slide 25: Example
C2
LD
ST
ACQ
ACQ
REL
LD
LD
CAS
LD
Thread 1
Thread 2
Thread 3
Core 1
Core 2
Core 3
16
0
0
Valid
Invalid
C3
Registered
Shared Cache
Backoff
HIT
C2
LD

## Slide 26: Example
Hardware backoff reduces cache misses from Read-Read races
C2
LD
ST
ACQ
ACQ
REL
LD
LD
CAS
LD
Thread 1
Thread 2
Thread 3
Core 1
Core 2
Core 3
Registered
16
0
0
Valid
Invalid
C3
Invalid
Registered
Shared Cache
Backoff
HIT
C2
LD

## Slide 27: Outline
Motivation
Background: DeNovo Coherence for Data
DeNovoSync Design
Experiments
  Methodology
  Qualitative Analysis
  Results
Conclusions

## Slide 28: Methodology
Compared MESI vs. DeNovoSync0 vs. DeNovoSync
Simics full-system simulator
  GEMS and Garnet for memory and network simulation
16 and 64 cores (in-order)
Metrics: Execution time, network traffic
Workloads
  24 synchronization kernels
    Lock-based: Test&Test&Set and array locks
    Non-blocking data structures
    Barriers: centralized and tree barriers, balanced and unbalanced
  13 application benchmarks
    From SPLASH-2 and PARSEC 3.1
Annotated data sharing statically (choice orthogonal to this paper)

## Slide 29: Qualitative Analysis
Analyze costs (execution time, traffic) in two parts
  Linearization point
    Ordering of linearization instruction = ordering of method
    Usually on critical path
  Pre-linearization points
    Non-linearization instructions (do not determine ordering)
    Usually checks, not on critical path
CAS
LD
.
.
.
LD
ACQ
LD
LD
.
.
.

## Slide 30: Qualitative Analysis Example (1 of 2)
Multiple readers, one succeeds: Test&Test&Set locks
 | Linearization | Pre-linearization
MESI |  | 
DeNovoSync0 |  | 
DeNovoSync |  | 

## Slide 31: Qualitative Analysis Example (1 of 2)
Multiple readers, one succeeds: Test&Test&Set locks
 | Linearization | Pre-linearization
MESI | Release has high inv overhead, on critical path to next acquire | 
DeNovoSync0 |  | 
DeNovoSync |  | 

## Slide 32: Qualitative Analysis Example (1 of 2)
Multiple readers, one succeeds: Test&Test&Set locks
 | Linearization | Pre-linearization
MESI | Release has high inv overhead, on critical path to next acquire | 
DeNovoSync0 | No inv overhead | 
DeNovoSync |  | 

## Slide 33: Qualitative Analysis Example (1 of 2)
Multiple readers, one succeeds: Test&Test&Set locks
 | Linearization | Pre-linearization
MESI | Release has high inv overhead, on critical path to next acquire | 
DeNovoSync0 | No inv overhead | 
DeNovoSync | No inv overhead | 

## Slide 34: Qualitative Analysis Example (1 of 2)
Multiple readers, one succeeds: Test&Test&Set locks
 | Linearization | Pre-linearization
MESI | Release has high inv overhead, on critical path to next acquire | Local spinning
DeNovoSync0 | No inv overhead | 
DeNovoSync | No inv overhead | 

## Slide 35: Qualitative Analysis Example (1 of 2)
Multiple readers, one succeeds: Test&Test&Set locks
 | Linearization | Pre-linearization
MESI | Release has high inv overhead, on critical path to next acquire | Local spinning
DeNovoSync0 | No inv overhead | Read-Read races, but not on critical path
DeNovoSync | No inv overhead | 

## Slide 36: Qualitative Analysis Example (1 of 2)
Multiple readers, one succeeds: Test&Test&Set locks
 | Linearization | Pre-linearization
MESI | Release has high inv overhead, on critical path to next acquire | Local spinning
DeNovoSync0 | No inv overhead | Read-Read races, but not on critical path
DeNovoSync | No inv overhead | Backoff mitigates Read-Read races
DeNovo expected to be better than MESI
Similar analysis holds for non-blocking constructs

## Slide 37: Qualitative Analysis Example (2 of 2)
Many readers, all succeed: Centralized barriers
  MESI: high linearization due to invalidations
  DeNovo: high linearization due to serialized read registrations
One writer, one reader: Tree barriers, array locks
  DeNovo, MESI comparable to first order
Qualitative analysis only considers synchronization
  Data effects: Self-invalidation, coherence granularity, …
  Orthogonal to this work, but affect experimental results

## Slide 38: Synchronization Kernels: Execution Time (64 cores)
For 44 of 48 cases, 22% lower exec time, 58% lower traffic (not shown)
Remaining 4 cases:
  Centralized unbalanced barriers: But tree barriers better for MESI too
  Heap with array locks: Need dynamic data signatures for self-invalidation
Test&Test&Set locks
Array locks
Non-blocking struct
Barriers
Chart: 
| M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | M | DS0 | DS | single Q | stack | heap | single Q | stack | heap | M-S queue | Herlihy stack | Herlihy heap | tree (UB) | central (UB)
 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0.99996 | 0 | 0 | 1 | 0 | 0 | 1 | 1
 | 0.54806 | 0.54961 | 0.59197 | 0.71761 | 0.76736 | 1.1306 | 0 | 1.6178 | 0 | 0 | 1.127 | 0 | 0 | 2.177 | 0 | 0.9523 | 1.1445
 | 0.49037 | 0.47663 | 0.507 | 0.71753 | 0.76688 | 1.1306 | 0 | 0 | 0.89198 | 0 | 0 | 0.60636 | 0 | 0 | 0.87987 | 0.9523 | 1.1445

## Slide 39: Applications (64 cores)
For 12 of 13 cases, 4% lower exec time, 24% lower traffic
Memory time dominated by data (vs. sync) accesses
Chart: 
| M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | FFT | LU | black scholes | swaptions | radix | bodytrack | barnes | water | ocean | fluid animate | canneal | ferret | x264
 | 1 | 1.014 | 1 | 0.95724 | 1 | 0.99234 | 1 | 0.9989 | 1 | 1.0226 | 1 | 1.0146 | 1 | 1.0021 | 1 | 0.86451 | 1 | 0.67629 | 1 | 1.0696 | 1 | 1.0099 | 1 | 0.90199 | 1 | 0.99657
sw backoff stall cycles
Chart: 
| M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | M | DS | FFT | LU | black scholes | swaptions | radix | bodytrack | barnes | water | ocean | fluid animate | canneal | ferret | x264
 | 1 | 0.56379 | 1 | 0.70528 | 1 | 0.56316 | 1 | 0.50398 | 1 | 0.96762 | 1 | 0.83093 | 1 | 0.85929 | 1 | 0.81978 | 1 | 0.78586 | 1 | 0.96101 | 1 | 0.84716 | 1 | 0.64378 | 1 | 0.79053
Execution Time
Barriers (64 cores)
Network Traffic

## Slide 40: Conclusions
DeNovoSync: First to cache arbitrary synch w/o writer-initiated inv
  Registered reads + hardware backoff
With simplicity, performance, energy advantages of DeNovo
  No transient states, no directory storage, no inv/acks, no false sharing, …
DeNovoSync vs. MESI
  Kernels: For 44 of 48 cases, 22% lower exec time, 58% lower traffic
  Apps: For 12 of 13 cases, 4% lower exec time, 24% lower traffic
 Complexity-, performance-, energy-efficiency w/o s/w restrictions
Future: DeNovo w/ heterogeneity [ISCA’15], dynamic data signatures