## Slide 1: Hardware Fault Recovery for I/O Intensive Applications
Pradeep Ramachandran, Intel Corporation,
Siva Kumar Sastry Hari, NVDIA
Manlap (Alex) Li, Latham and Watkins LLP
Sarita V. Adve, University of Illinois at Urbana Champaign
*This work was done when Pradeep, Siva, and Alex were
at the University of Illinois at Urbana Champaign

## Slide 2: Battling the Dark Side of Moore’s Law
Hardware will fail in the field for a variety of reasons
Need in-the-field solutions for detection, diagnosis, and recovery
  Must incur low-cost => traditional redundancy solutions too expensive!
SWAT: A low-cost solution to handle unreliable HW
  Key: Handle only HW faults that affect SW, near-zero impact to fault-free exec
  Detect faults with near-zero cost monitors for SW anomaly, smart HW recovery
This paper: A closer look at fault recovery with low-cost detection
Transient errors
(High-energy particles )
Wear-out failures
(Devices are weaker)
… and so on
Intermittent
fault

## Slide 3: Components of SWAT
Detection: Low-cost monitors for anomalous SW behavior
  E.g., fatal traps from protection violation, div by zero [ASPLOS’08, DSN‘08, ASPLOS‘12]
Diagnosis: Identifies faulty core, uarch block [DSN‘08, MICRO’09]
Recovery w/o IO: Leverage existing sol for core/mem chkpt, rollback
Recovery with IO not handled; also ignored by most other prior work
Intricate relationship between detection and recovery not considered
  Checkpoint interval = maximum detection latency
Error
Symptom
detection
Fault
Chkpt
Diagnosis
Recovery
Chkpt

## Slide 4: Contributions of This Paper
HW technique for fault recovery in the presence of external IOs
  Existing recovery solutions mostly ignore the “output commit” problem
  Low overhead to fault-free exec ⇒ detection latency <100K instructions
New definition of detection latency to be more relevant to recovery
  @100K instructions, only 80% of faults detected with existing definition!
  Existing definition conservative ⇒ high-overhead to fault-free execution
Combined evaluation of low-cost fault detection & recovery solution
  SWAT recovers the system for 94% of injected faults @ 100K instr, 0.2% SDC rate

## Slide 5: Agenda
Motivation and Contributions
Recovery in the presence of external IO
A new definition of detection latency
Combined evaluation of detection and recovery
Conclusions

## Slide 6: Output Buffering
External outputs need to be delayed until guaranteed to be fault-free
  Once committed, they cannot be rolled-back
Previous solution: Buffer outputs in dedicated SW [Revive I/O]
  No HW changes, exploit semantics of SW-level output for efficiency
  Outputs vulnerable as buffering SW runs on faulty HW
Our solution: Buffer external outputs in dedicated HW
  SW output maps to multiple dependent HW stores ⇒ potentially high overheads
  Solution should require no changes to device HW
  Buffered outputs should not be vulnerable to HW faults
Notes: Don’t say anything about challenges. These are just key questions that need to be answered here

## Slide 7: Architecture of HW Output Buffer
CPU communicates with devices through I/O loads & stores
HW buffer buffers outputs until next checkpoint or IO fence
  Committed outputs verified fault-free and drained in parallel to regular execution
Buffered outputs protected through ECC checks
  Special handling during DMA transfer to device to protect output while draining
CPU-centric implementation with no changes to IO devices
CPU
Memory
$
Device
Device
Device
OUTPUT
BUFFER
Memory
Bus
IO Bus

## Slide 8: Operations of HW Output Buffer
Fault-free Operation
  Outputs verified as fault-free at second subsequent checkpoint
Recovery Operation
St 1
St 2
Drain Stores
in background
Dev
St 1
Dev
St 2
Buffer
St 1
St 2
Fault
Detection
Dev
St 3
Buffer
Discard st3
Dev
St 1
Dev
St 2
Buffer Stores
to Devices
Rollback Arch state
St 1
St 2
Dev
St 3
Restore Devices
Continue execution from this point
Determined by
Maximum Detection latency
Notes: Rely on the fact that device outputs are idempotent

## Slide 9: Measuring Fault-free Overheads
Buffering outputs imparts overheads to fault-free execution
  Outputs to clients delayed  performance overhead
  HW to store buffered outputs  area overhead
Simulated a fault-free client-server system to measure overheads
Focused on I/O intensive workloads to study fault free overheads
  sshd, apache, mysql, squid w/ multiple request and server threads
Network
CPU
Devices
CPU
Devices
HW
Output
Buffer
Simulated Server
Simulated Client
SIMICS full-system simulator
Latency = 0.1ms

## Slide 10: Performance Overhead from Output Buffering
Chart: Checkpoint Interval (in instructions)
| 10K | 100K | 1M | 2M | 5M | 10M
apache | 1 | 1.0001 | 1.5698 | 3.1864 | 15.2387 | 18.9924
sshd | 0.80439 | 1.0089 | 1.2022 | 1.4135 | 2.3774 | 4.0914
squid | 0.99524 | 1.0392 | 5.4589 | 11.6925 | 31.331 | 62.6228
mysql | 0.91913 | 1.0106 | 1.5008 | 2.1273 | 3.9225 | 7.3894
Chkpt interval of 1M inst (~1ms) => perf impact of 5X! Grows with chkpt interval!
Practical chkpt interval <100K inst (~100us); perf overhead of <5% on fault-free exec
Notes: Remember that here there is no opal/ruby. Practicality of this is limited.

## Slide 11: Connecting Detection and Recovery
Checkpoint interval determined by maximum detection latency
Recovery results  checkpoint interval ≤100K instructions
  <5% performance overhead, <2KB area overhead
SWAT detection results  only 80% detected in 100K instructions
Need to reduce latency to enable practical solution
  Shortcoming identified only when components combined, ignored in prior work
Strategy
  New low-cost HW detector for out-of-bounds accesses (details in paper)
  Re-look at detection latency for recovery; previous definitions too conservative

## Slide 12: Agenda
Motivation and Contributions
Recovery in the presence of external IO
A new definition of detection latency
Combined evaluation of detection and recovery
Conclusions

## Slide 13: A New Definition for Detection Latency
Traditional def: Hard latency = arch state corruption to detection
But do all faults that corrupt arch state make system unrecoverable?
Key observation: Software may tolerate some corruptions!
  E.g., a used only for a>0 changes from 5 to 10
New definition: Soft latency = SW state corruption to detection
  Checkpoint interval should be based on new definition
Bad SW state
Soft Latency
Bad arch state
Hard latency
Fault
Detection
Recoverable
chkpt
Recoverable
chkpt
Notes: Although our evaluation of new latency is using periodic rollbacks, a real system does not have to do this.

## Slide 14: Hard-Latency vs Soft-Latency to Determine Checkpoint Interval
For any targeted detection rate, detection latency w/ Hard-latency >> w/ Soft-latency
 Hard-latency may result in unnecessarily high chkpt intervals, high overheads

## Slide 15: Agenda
Motivation and Contributions
Recovery in the presence of external IO
A new definition of detection latency
Combined evaluation of detection and recovery
Conclusions

## Slide 16: Evaluating SWAT Detection + Recovery with IO Devices
µarch-level fault injections into simulated server CPU
  Focused on server workloads due to heavy I/O
Detection: Simulate faults for 10M instructions with SWAT detectors
Recovery: Restore system after detection with different chkpt intervals
  Rollback CPU & memory, restore devices, replay buffer outputs
Network
CPU
Devices
CPU
Devices
HW
Output
Buffer
Simulated Server
Simulated Client
SIMICS full-system simulator
Latency = 0.1ms
Fault
Notes: Mention how we can implement device restoration and how we do it in our implementation. Should we instead put a separate slide for this?

## Slide 17: SWAT Detection + Recovery Results
94% of faults detected and recovered at chkpt interval of 100K instructions
Only 44/18,000 injected faults (0.2%) cause Silent Data Corruptions (SDCs)
Chart: Permanent Faults
| 10K | 100K | 1M | 10M
Masked | 317 | 338 | 614 | 1919
Detected + Recovered | 7521 | 7834 | 7638 | 6704
Detected + Unrecovered | 833 | 693 | 643 | 300
Potential SDC | 267 | 82 | 40 | 36
Chart: Transient Faults
| 10K | 100K | 1M | 10M
Masked | 7731 | 7724 | 7750 | 7858
Detected + Recovered | 924 | 938 | 965 | 936
Detected + Unrecovered | 205 | 212 | 151 | 95
Potential SDC | 70 | 46 | 59 | 65

## Slide 18: Conclusions
Key challenge: Low-cost solution for reliable exec on unreliable HW
Emerging low-cost sol. for detection, recovery, diagnosis, like SWAT
But recovery in the presence of IO ignored ⇒ limited applicability
This paper presents
  Low-cost HW solution for recovery with IO; <5% perf, <2KB area overhead
  New definition of detection latency that reduces overheads to fault-free exec
  Eval of detection + recovery; only 0.2% of faults cause SDC @ above overheads
On-going work: Eliminate SDCs by leveraging application properties

## Slide 19: Hardware Fault Recovery for I/O Intensive Applications
Pradeep Ramachandran, Intel Corporation
Siva Kumar Sastry Hari, NVDIA
Manlap (Alex) Li, Latham and Watkins LLP
Sarita V. Adve, University of Illinois at Urbana Champaign
*This work was done when Pradeep, Siva, and Alex were
at the University of Illinois at Urbana Champaign

## Slide 20: backup

## Slide 21: I/O Characteristics of Server Workloads
Application | Data Transferred | Average Rate | % I/O wait
apache | 38MB | 9.5MBps | 76.5%
sshd | 19MB | 2.5MBps | 24.3%
squid | 20MB | 11.6MBps | 69.5%
mysql | 7.5MBps | 1.05MBps | 71.1%

## Slide 22: Importance of I/O for Fault Recovery
No device recovery, output buffering reduces recoverability by 89%
Chart: Permanent Faults
| Full | No Dev | No I/O | Full | No Dev | No I/O | Full | No Dev | No I/O | Full | No Dev | No I/O | 10K | 100K | 1M | 10M
Masked | 317 | 317 | 318 | 338 | 336 | 335 | 614 | 613 | 342 | 1919 | 1919 | 353
Recovered | 7621 | 5938 | 5525 | 7934 | 4885 | 4467 | 7738 | 4177 | 4160 | 6804 | 4292 | 4276
DUE | 733 | 2413 | 2848 | 593 | 3644 | 4083 | 543 | 4089 | 4418 | 200 | 2715 | 4307
Potential SDC | 267 | 271 | 265 | 82 | 82 | 70 | 40 | 37 | 36 | 36 | 34 | 20

## Slide 23: Measuring Soft Latency vs Hard Latency
Identify uarch state corruption easy  hard latency easily measurable
Measuring soft latency  need to identify when SW state is corrupted
But identifying SW state corruption is hard!
  Need to know how faulty value used by application, and if it affects output
Measure soft latency by rolling back to older checkpoints
  Only for analysis, not required in reality
Fault
Detection
Bad arch state
Bad SW state
Soft latency
Chkpt
Rollback &
Replay
Symptom
Chkpt
Fault effect
masked
Rollback &
Replay