## Slide 1: Approximate Computing: (Old) Hype or New Frontier?
Sarita Adve
University of Illinois, EPFL
Acks: Vikram Adve, Siva Hari, Man-Lap Li, Abdulrahman Mahmoud, Helia Naemi, Pradeep Ramachandran, Swarup Sahoo, Radha Venkatagiri, Yuanyuan Zhou

## Slide 2: What is Approximate Computing?
Trading output quality for resource management?
Exploiting applications’ inherent ability to tolerate errors?
Old?
GRACE [2000-05] rsim.cs.illinois.edu/grace
SWAT [2006- ] rsim.cs.illinois.edu/swat
  Many others
Or something new?
  Approximate computing through the lens of hardware resiliency …

## Slide 3: Motivation
Redundancy
Overhead (perf., power, area)
Reliability
Goal: High reliability at low-cost

## Slide 4: SWAT: A Low-Cost Reliability Solution
Need handle only hardware faults that affect software
 Watch for software anomalies (symptoms)
    Zero to low overhead “always-on” monitors
Diagnose cause after anomaly detected and recover
    May incur high overhead, but invoked infrequently
     SWAT: SoftWare Anomaly Treatment

## Slide 5: SWAT Framework Components
Detection: Monitor symptoms of software misbehavior
Diagnosis: Rollback/replay on multicore
Recovery: Checkpoint/rollback or app-specific action on acceptable errors
Repair/reconfiguration: Redundant, reconfigurable hardware
Flexible control through firmware
Fault
Error
Anomaly
detected
Recovery
Diagnosis
Repair
Checkpoint
Checkpoint

## Slide 6: SWAT Framework Components
Detection: Monitor symptoms of software misbehavior
Diagnosis: Rollback/replay on multicore
Recovery: Checkpoint/rollback or app-specific action on acceptable errors
Repair/reconfiguration: Redundant, reconfigurable hardware
Flexible control through firmware
Fault
Error
Anomaly
detected
Recovery
Diagnosis
Repair
Checkpoint
Checkpoint
How to bound silent (escaped) errors?
When is an error acceptable (at some utility) or unacceptable?
How to trade silent errors with resources?
How to associate recovery actions with errors?

## Slide 7: Advantages of SWAT
Handles only errors that matter
  Oblivious to masked error, low-level failure modes, software-tolerated errors
Low, amortized overheads
  Optimize for common case, exploit software reliability solutions
Customizable and flexible
  Firmware control can adapt to specific reliability needs
Holistic systems view enables novel solutions
  Software-centric synergistic detection, diagnosis, recovery solutions
Beyond hardware reliability
  Long term goal: unified system (HW+SW) reliability
  Systematic trade off between resource usage, quality, reliability

## Slide 8: SWAT Contributions (for in-core hw faults)
In-situ Diagnosis [DSN’08]
Trace-based µarch diagnosis
Fault Detection
Very low cost detectors [ASPLOS’08, DSN’08]
Bound silent errors [ASPLOS’12, DSN’12]
Identify error outcomes: Relyzer, GangES [ISCA’14]
Diagnosis
Fault
Error
Symptom
detected
Recovery
Repair
Chkpt
Chkpt
Error modeling
SWAT-Sim [HPCA’09]
FPGA-based [DATE’12]
mSWAT [MICRO’09]
Multicore detection & diagnosis
Fault Recovery
Handling I/O [TACO’15]
Complete solution for in-core faults, evaluated for variety of workloads

## Slide 9: SWAT Fault Detection
Simple monitors observe anomalous SW behavior [ASPLOS’08, MICRO’09]
Very low hardware area, performance overhead
SWAT firmware
Fatal Traps
Division by zero,
RED state, etc.
Kernel Panic
OS enters panic
state due to fault
High OS
High contiguous
OS activity
Hangs
Simple HW hang
detector
App Abort
App abort due
to fault
Out of Bounds
Flag illegal addresses

## Slide 10: Evaluating SWAT Detectors So Far
Full-system simulation with out-of-order processor
  Simics functional + GEMS timing simulator
  Single core, multicore, distributed client-server
Apps: Multimedia, I/O intensive, & compute intensive
  Errors injected at different points in app execution
µarch-level error injections (single error model)
  Stuck-at, transient errors in latches of 8 µarch units
  ~48,000 total errors

## Slide 11: Error Outcomes
APPLICATION
.
.
.
Output
Symptom
APPLICATION
.
.
.
Output
Transient error
APPLICATION
.
.
.
Output
Symptom detectors (SWAT):
Fatal traps, kernel panic, etc.
Output
Masked
Silent Data Corruption (SDC)
Detection
Acceptable Unacceptable
(w/ some quality)

## Slide 12: SWAT SDC Rates
SWAT detectors effective
<0.2% of injected µarch errors give unacceptable SDCs (109/48,000 total)
BUT hard to sell empirically validated, rarely incorrect systems
Chart: Total injections
| SPEC | Server | Media | SPEC | Server | Media | Permanents | Transients
Masked | 1965 | 606 | 799 | 7520 | 7675 | 3804
Detected | 6937 | 8295 | 7495 | 909 | 1239 | 324
App-Tolerated | 47 | 4 | 85 | 15 | 6 | 31
SDC | 7 | 12 | 17 | 19 | 31 | 23

## Slide 13: Challenges
Redundancy
Overhead (perf., power, area)
Reliability
How?
Tunable
reliability
SWAT
Very high
reliability at low-cost
Goals:
Full reliability at low-cost
Accurate reliability evaluation
Tunable reliability vs. quality vs. overhead

## Slide 14: Research Strategy
Towards an Application Resiliency Profile
  For a given instruction what is the outcome of an error?
  For now, focus on a transient error in single bit of register
Convert SDCs into (low-cost) detections for full reliability and quality
OR let some acceptable or unacceptable SDCs escape
  Quantitative tuning of reliability vs. overhead vs. quality

## Slide 15: Challenges and Approach
Determine error outcomes for all application-sites
Cost-effectively convert (some) SDCs to Detections
APPLICATION
.
.
Output
APPLICATION
.
.
Output
SDC-causing
error
APPLICATION
.
Error Detection
Error Detectors
Challenges:
What to use?
Where to place?
How to tune?
How?
Complete app
resiliency evaluation
How?
Challenge: Analyze all errors with few injections
Impractical, too many injections
>1,000 compute-years for one app

## Slide 16: Relyzer: Application Resiliency Analyzer [ASPLOS’12]
APPLICATION
.
.
.
Output
Prune error sites
Application-level
error (outcome) equivalence
Predict error outcome if possible
Inject errors for remaining sites
Equivalence Classes
Pilots
Relyzer
APPLICATION
.
.
Output
Can list virtually all SDC-causing instructions

## Slide 17: Def to First-Use Equivalence
Fault in first use is equivalent to fault in def  prune def
  r1 = r2 + r3
  r4 = r1 + r5
  …
If there is no first use, then def is dead  prune def
Def
First use

## Slide 18: Control Flow Equivalence
  Insight: Errors flowing through similar control paths may behave similarly
CFG
X
Errors in X that take path behave similarly
Heuristic: Use direction of next 5 branches

## Slide 19: Store Equivalence
Insight: Errors in stores may be similar if stored values are used similarly
Heuristic to determine similar use of values:
  Same number of loads use the value
  Loads are from same PCs
Store
Memory
PC1
PC2
Load
Load
Store
PC1
PC2
Load
Load
Instance 1
Instance 2
PC
PC

## Slide 20: Relyzer
Relyzer: A tool for complete application resiliency analysis
  Employs systematic error pruning using static & dynamic analysis
  Currently lists outcomes of masked, detection, SDC
3 to 6 orders of magnitude fewer error injections for most apps
  99.78% error sites pruned, only 0.004% sites represent 99% of all sites
  GangES speeds up error simulations even further [ISCA’14]
Can identify virtually all SDC causing error sites
What about unacceptable vs. acceptable SDC? Ongoing
APPLICATION
.
.
Output
Relyzer
APPLICATION
.
.
Output

## Slide 21: Can Relyzer Predict if SDC is Acceptable?
Pilot = Acceptable SDC 
  All faults in class = Acceptable SDCs ???
Pilot = Acceptable SDC with quality Q 
  All faults in class = Acceptable SDCs with quality Q ???
Equivalence
Classes
Pilots

## Slide 22: PRELIMINARY Results for Utility Validation
Pilot = Acceptable SDC with quality Q 
  All faults in class = Acceptable SDCs with quality Q ???
Studied several quality metrics
  E.g., E = abs(percentage average relative error in output components),
  capped to 100%
  Q = 100 - E (> 100% error gives Q=0, 1% gives Q=99)
 

## Slide 23: Research Strategy
Towards an Application Resiliency Profile
  For a given instruction what is the outcome of a fault?
  For now, focus on a transient fault in single bit of register
Convert SDCs into (low-cost) detections for full reliability and quality
OR let some acceptable or unacceptable SDCs escape
  Quantitative tuning of reliability vs. overhead vs. quality

## Slide 24: SDCs → Detections [DSN’12]
What to
protect?
-
SDC-causing fault sites
How to
Protect?
Low
-
cost detectors
Where to place?
Many errors propagate to
few program values
What detectors?
Program
-
level properties tests
Uncovered
fault
-
sites?
Selective instruction
-
level duplication

## Slide 25: Insights for Program-level Detectors
Goal: Identify where to place the detectors and what detectors to use
Placement of detectors (where)
  Many errors propagate to few program values
    End of loops and function calls
Detectors (what)
  Test program-level properties
    E.g., comparing similar computations and checking value equality

## Slide 26: Loop Incrementalization
A = base addr. of a
B = base addr. of b
L: load r1 ← [A]
. . .
load r2 ← [B]
. . .
store r3 → [A]
. . .
add A = A + 0x8
add B = B + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code

## Slide 27: Loop Incrementalization
A = base addr. of a
B = base addr. of b
L: load r1 ← [A]
. . .
load r2 ← [B]
. . .
store r3 → [A]
. . .
add A = A + 0x8
add B = B + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code
Where: Errors from all iterations propagate here in few quantities
What: Property checks on A, B, and i
Diff in A = Diff in B
Diff in A = 8 Diff in i
Collect initial values of A, B, and i
SDC-hot app sites
No loss in coverage - lossless

## Slide 28: Registers with Long Life
Some long lived registers are prone to SDCs
For detection
  Duplicate the register value at its definition
  Compare its value at the end of its life
No loss in coverage - lossless
Life
time
R1 definition
Copy
Use 1
Compare
Use 2
Use n
.
.
.

## Slide 29: Converting SDCs to Detections: Results
Discovered common program properties around most SDC-causing sites
Devised low-cost program-level detectors
  Average SDC reduction of 84%
  Average cost of 10%
New detectors + selective duplication = Tunable resiliency at low-cost
  Found near optimal detectors for any SDC target
Chart: SDC reduction

## Slide 30: Identifying Near Optimal Detectors: Naïve Approach
Bag of detectors
SDC coverage
SFI
50%
Example: Target SDC coverage = 60%
Sample 1
Overhead = 10%
Sample 2
Overhead = 20%
SFI
65%
Tedious and time consuming

## Slide 31: Identifying Near Optimal Detectors: Our Approach
Bag of detectors
Selected Detectors
SDC Covg.= X%
Overhead = Y%
Detector
1. Set attributes, enabled by Relyzer
2. Dynamic programming
Constraint: Total SDC covg. ≥ 60%
Objective: Minimize overhead
Overhead = 9%
Obtained SDC coverage vs. Performance trade-off curves [DSN’12]

## Slide 32: SDC Reduction vs. Overhead Trade-off Curve
Consistently better over pure instruction-level duplication (w/ Relyzer)
But overhead still significant for very high resilience
Remove protection overhead for acceptable (bounded) quality loss?
Our detectors + Redundancy
Pure Redundancy
Chart: SDC Reduction
18%
90%
24%
99%
(For Relyzer identified SDCs)

## Slide 33: Understanding Quality Outcomes with Relyzer (Prelim Results)
Promising potential, but quality metric and application dependent
Can use to quantitatively tune quality vs. reliability vs. resources

## Slide 34: Quality Outcomes – An Instruction-Centric View
Systems operate at higher granularity than error sites: Instruction?
When is an instruction approximable?
  Which errors in instruction should result in acceptable outcome?
    All? Single-bit errors in all register bits? Single-bit errors in subset of bits?
  When is an outcome acceptable?
    Best case : all errors that are masked or produce SDCs are acceptable

## Slide 35: So - (Old) Hype or New Frontier?
SWAT inherently implies quality/reliability relaxation aka approx. computing
Key: Bound quality/reliability loss? (Subject to resource constraint)
  Can serve as enabler for widespread adoption of resilience approach
  Especially if automated
Some other open questions
  Instruction vs. data-centric?
  Resiliency profiles and analysis at higher granularity?
  How to compose?
  Impact on recovery?
  Other fault models?
Software doesn’t ship with 100% test coverage, why should hardware?

## Slide 36: Summary
Overhead (perf., power, area)
Reliability
Tunable
reliability
SWAT
Very high
reliability at low-cost
SWAT symptom detectors: <0.2% SDCs at near-zero cost
Relyzer: Systematically find remaining SDC-causing app-sites
Convert SDCs to detections with program-level detectors
Tunable reliability vs. overhead
Ongoing: Add tunable quality, Relyzer validations promising