## Slide 1
Radha Venkatagiri1, Abdulrahman Mahmoud1,
Siva Kumar Sastry Hari2, Sarita Adve1
1University of Illinois at Urbana-Champaign, 2NVIDIA Research
Approxilyzer:
Towards A Systematic Framework for Instruction-Level Approximate Computing and its Application to Hardware Resiliency
Let them eat
cake!
Make Informed Choices!
Notes: Good afternoon, I am Radha Venkatagiri from the University of Illinois and my talk today is about Approxilyzer, a systematic framework for approximate computing.

## Slide 2: Introduction
Error in program
11% degradation
Quality of output
APPROXILYZER
Final
end-to-end Output
?
Approximate computing
  Trades off output quality for power, performance, resilience...
Fundamental problem: How do errors in a program affect its output quality?
Notes: The end of conventional scaling has led to the popularity of approximate computing, which trades off output quality for power and performance.
For the widespread adoption of approximate computing, a fundamental requirement is to understand how perturbations or errors in a program’s execution affects the quality of the final output produced.
In this talk I’ll show you how we can solve this problem using a tool called Approxilyzer that determines the quality of the output produced when errors are introduced in the program’s execution.

## Slide 3: Contributions (1 of 2): Approxilyzer
APPROXILYZER
Final
end-to-end Output
End-to-end Quality Metric
(domain-specific)
+
+
Quality Threshold (Optional)
Unmodified Program
Approxilyzer: Tool to determine output quality
  Minimal programmer burden, general-purpose, automatic, comprehensive
Notes: Approxilyzer takes any unmodified general purpose program as input and requires the user to provide only the quality metric and optionally a quality threshold. The quality metric is a domain specific parameter and as such a minimal input required by any system that measures quality.

## Slide 4: Contributions (1 of 2): Approxilyzer
APPROXILYZER
Final
end-to-end Output
End-to-end Quality Metric
(domain-specific)
+
+
Quality Threshold (Optional)
Unmodified Program
Approxilyzer: Tool to determine output quality
  Minimal programmer burden, general-purpose, automatic, comprehensive
  Error Model: Single bit errors in operand register + dynamic instructions
Error site : Operand register bit + dynamic instruction
  Determine output quality with high accuracy (95%) and confidence (99%)
Notes: Taking these, Approxilyzer automatically quantifies how an single error in the program impacts the quality of its final end-to-end output.
The error model we consider in this work is single bit flips in operand registers of dynamic instructions. We use the term error site to refer to the location where an error can occur, namely specific register bits in specific dynamic instructions.
We show that Approxilyzer can determine the output quality produced by a given error with high accuracy and confidence.

## Slide 5: Contributions (1 of 2): Approxilyzer
APPROXILYZER
End-to-end Quality Metric
(domain-specific)
+
+
Quality Threshold (Optional)
Unmodified Program
Approxilyzer: Tool to determine output quality
  Minimal programmer burden, general-purpose, automatic, comprehensive
Comprehensive output quality profile
  Determine output quality with high accuracy (95%) and confidence (99%)
Notes: Moreover, Approxilyzer does this for virtually ALL such errors in the program allowing us to automatically build a comprehensive output quality profile for any general purpose program. So now we have the ability to forecast, for example, that a single bit perturbation in dynamic instruction X will lead to a maximum quality loss of say, 6% in the final output.

## Slide 6
  Ultra-low cost resiliency with approximate output
  Tuning output quality vs. resiliency coverage vs. cost
  Significant overhead savings (upto 55%) for small quality loss (1%)
  First order approximation potential of applications
  Identify potential approximable instructions, reduce exploration space
  40% static instructions have approximable 32b register chunks
Contributions (2 of 2): Applications of Approxilyzer
System Optimization; e.g.,
Resiliency vs. Cost vs. Quality
Optimizer
Identify potentially approximable instructions
End-to-end Quality Metric
+
APPROXILYZER
+
(Optional)
Quality Threshold
Unmodified Program
Comprehensive output quality profile
Notes: This ability is quite powerful and we demonstrate two example applications in this work. First we show how Approxilyzer can be used to tune output quality loss with respect to resiliency parameters to enable ultra-low cost resiliency solutions. We show that significant reductions in resiliency overheads can be achieved if the user is willing to tolerate very small losses in quality.
Second, more broadly, we demonstrate how Approxilyzer can provide a first order estimate of the approximation potential of any general purpose program automatically. This enables programmers or other tools to focus on just the promising subset of approximable instructions, identified by Approxilyzer, for further analysis. For example, we show that in the best case scenario, with virtually no quality threshold, on average, 40% of static instructions in our applications have at least one 32 bit register chunk that could be a candidates for approximation

## Slide 7: Outline
Introduction
Background: Relyzer
Approxilyzer
Application : Ultra-low cost resiliency
Application : First order approximation potential
Conclusion
Notes: The remainder of the talk is organized as follows. I’ll first provide some background about prior work we leverage, before describing the design details of Approxilyzer. I will then discuss the two applications of Approxilyzer before concluding.

## Slide 8: Challenge : Determine Quality Impact of All Errors
APPLICATION
.
.
.
Output
APPLICATION
.
.
.
Output
11% quality degradation
Challenge : Determine quality impact of virtually all errors in reasonable time
Notes: It is relatively simple to determine the impact of a single error. You inject the error in program execution and observe the output quality at the end. But being able to do so for all such errors, which amount to trillions in a program is prohibitive in time. To meet this challenge we leverage prior work called Relyzer that solves a similar problem.

## Slide 9: Background : Error Outcomes for Single Bit Errors
Error-free
execution
Output
Output
Output
Silent Data
Corruption (SDC)
Detection
Detection
Masked
ERROR ( )
Notes: Traditionally, the outcomes of an error in an execution is classified as either Masked, where the correct output is produced, or detected, where while the program produces catastrophic results like a segmentation fault or kernel panics, there are low cost mechanisms to detect that an error occurred. And finally silent data corruptions or SDC, where an incorrect output is produced. SDCs are the worst outcome of an error since they can neither be ignored nor can be protected by low cost mechanisms.

## Slide 10: Background: Relyzer [ASPLOS’12]
APPLICATION
.
.
.
Output
Equivalence Classes (using data + control flow heuristics)
Pilots
Few injections to predict the outcome of virtually all errors
  Insight: Errors flowing through similar control+data paths produce similar outcomes
Inject error in Pilot
Pilot outcome = Outcome of all errors in class
Notes: A prior tool called Relyzer which tries to predict the outcome (ie., masked, detected or SDC) of virtually all errors in a program, uses the insight that errors propagating through similar control and data paths, must behave similarly and hence produce similar outcomes.
It uses program analysis & heuristics to identify & group such similar errors together into equivalence classes. It then selects just one representative error from each class, called a Pilot and performs error injection it. The outcome of the pilot is then used to predict the outcome of all the errors in its equivalence class. Thus, Relyzer uses just a few error injections to predict the outcomes of virtually all errors in the program.

## Slide 11: Outline
Introduction
Background: Relyzer
Approxilyzer
Application : Ultra-low cost resiliency
Application : First order approximation potential
Conclusion
Notes: Next, I will describe how we leverage Relyzer and additional details of Approxilyzer.

## Slide 12: Approxilyzer : Predict SDC Quality
Not all SDCs (output corruptions) are bad – quality is important!
  Blackscholes: Precise = $100, SDC = $107, quality loss (relative error) = 7%
Pilot = SDC with quality Q  All errors in class = SDCs with quality Q?
Equivalence Classes
Pilots
APPLICATION
Output
.
.
.
Output Quality
SDC
11% Deviation from error-free o/p
11%
3% Deviation from error-free o/p
3%
67% Deviation from error-free o/p
67%
Comprehensive end-to-end output quality profile with few error injections
Notes: Relyzer’s analysis, while insightful, is quality unaware in that it assumes that all SDCs or output corruptions are unacceptable to the user.
Approxilyzer realizes that this is not the case, especially in approximate computing environments, and that quality is important in determining if a corrupted o/p is still acceptable to the user. To quickly give an example of what what I mean by output quality, consider the Parsec benchmark Blackscholes that produces a stock option price as an output. If the error free output is $100 and the SDC output is $107, using relative error as the quality metric, we can say that the quality is degraded by 7%.
The natural question that arises after looking at prior work is : Can Relyzer style equivalence classes can be used to predict quality? If yes, then we can inject errors in pilots, note the quality of the output produced and then use that to predict the output quality of all the errors in the equivalence class. In this way, with just a few error injections, we can build a comprehensive o/p quality profile.

## Slide 13: Approxilyzer: Quality Aware Error Classification
Granularity of quality?
  Hard to capture large range of continuous values, unnecessary!
Output
Silent Data Corruption (SDC)
Highly Tolerable
Error in non-significant o/p
Quality loss < 0.0001% etc.
Not Tolerable
Quality loss > 100%
Potentially tolerable
Quality > Threshold?
Record quality in fine-grained discretized bins
SDC-Good
SDC-Bad
SDC-Maybe
Detectable Data
Corruptions (DDC)
NaN, infinity etc.
Not approximable!
Notes: When we talk about determining the quality of SDC outputs, we have to ask at what granularity do we want a tool like Approxilyxer to capture quality?
It is a tall order and frankly unnecessary to ask any tool to finely capture the entire spectrum of a continuous parameter like quality. Surely, we can coarsen the granularity for at least some parts of the spectrum.
For example, a subclass of errors in the edge of the spectrum that produce non-sense outputs such as Nans and infinities, can actually be detected by placing low-cost detectors and we call them Detectable data corruptions or DDC. In the spectrum of the outputs that make sense, some errors produce such minute corruptions that we can reasonably assume that they would be acceptable to most users, and we classify them as SDC-Good. Similarly, on the other end, there are errors that produce such large quality degradations (for example greater than 100%) that we can reasonably say that they won’t be acceptable to most users. We call these collectively as SDC-Bad. In the middle are the error that we call SDC-Maybes because they maybe acceptable to users depending on their quality threshold. The SDC-Maybes are the space where most users will do their tuning and it is for this range that we need to determine and record quality at fine granularities. In Approxilyzer we record the quality by discretizing them into fine grained quality bins. For example, using relative error, quality degradation of 12.6% is rounded up to the nearest integer and assigned a quality bin of 13.
Depending on how the quality information is used, some of these other categories can be further coarsened. For example, since errors with SDC-Bad and DDC outcomes are both unacceptable to users, we can classify them together as belonging to error sites that are not approximable. We provide more details about the different types of coarsening in the paper.

## Slide 14: Approxilyzer: Validation
Pilot = SDC w quality Q
   All errors in class (Population) = SDCs w quality Q?
  Pilot error category == Population error category?
  For SDC-Maybe, pilot quality bin == population quality bin?
~ 2.6 million error injection experiments
99% confidence interval
Notes: To validate Approxilyzer, the question we ask is – how well does the Pilot predict the quality of the rest of the equivalence class? To answer this question, we perform error injections on a sample of errors from the equivalence classes, which we call the population and then we check if the coarse error category of the population and their corresponding pilot match. Additionally for SDC-Maybe errors, we also check if the quality bins of th pilot matches that of its population exactly. Overall we do around 2.6 million error injection experiments and our sampling rate has a statistical confidence of 99%.

## Slide 15: Approxilyzer : Validation
Chart: Approxilyzer Validation %
| Swaptions | LU | Blackscholes | FFT | Water | Average
Baseline | 99.4 | 95.4 | 87.4 | 59.6 | 97.8 | 87.92
On average, 88% prediction accuracy with exact quality bin match
Notes: With this baseline that I just described we see that prediction accuracy is 88%. ie, if the pilot produces a discretized quality degradation of 11%, then 88% of errors in its equivalence class also produce discretized quality of 11%. While this kind of precision is impressive, requiring the Quality bins to exactly match is unnessarily strict especially at quality bin boundaries.

## Slide 16: Approxilyzer : Validation
Chart: Approxilyzer Validation %
| Swaptions | LU | Blackscholes | FFT | Water | Average
Baseline | 99.4 | 95.4 | 87.4 | 59.6 | 97.8 | 87.92
Quality_Margin = 1 | 99.4 | 95.5 | 90 | 90.3 | 99.8 | 95
Allow Δ = 1 flexibility in quality bin matching
ΔQuality_Bin= 1
Notes: Allowing a small flexibility of +/- 1 in quality bin matching, improves the prediction accuracy to 95%. ie, if the pilot’s quality bin is 11, then equivalence class errors with quality bins ranging from 10 and 12 are considered correct.

## Slide 17: Approxilyzer : Validation
Chart: Approxilyzer Validation %
| Swaptions | LU | Blackscholes | FFT | Water | Average
Baseline | 99.4 | 95.4 | 87.4 | 59.6 | 97.8 | 87.92
Quality_Margin = 1 | 99.4 | 95.5 | 90 | 90.3 | 99.8 | 95
Quality_Margin = 2 | 99.4 | 95.5 | 90.3 | 97 | 99.8 | 96.4
High prediction accuracy (96%)
Quality determined at very fine granularity (within Δ=2 quality bins)
ΔQuality_Bin= 1
ΔQuality_Bin= 2
Notes: And increasing this flexibile quality window to a delta of 2, brings up the accuracy to 96%. Hence we show that Approxilyzer has high prediction accuracy and can determine quality at very fine granularities.

## Slide 18: Outline
Introduction
Background: Relyzer
Approxilyzer
Application : Ultra-low cost resiliency
Application : First order approximation potential
Conclusion
Notes: Next we demonstrate two uses of Approxilyzer.

## Slide 19: Approxilyzer Application to Resiliency
Tune quality vs. resiliency vs. overhead
  Enable ultra-low cost resiliency solutions
  Resiliency scheme: Instruction duplication
Selectively protect instructions
  End-to-end output quality is not acceptable to user/application
  Cannot be protected by low-cost detectors
SDC-Good
SDC-Bad
SDC-Maybe
Detectable Data
Corruptions (DDC)
User acceptable quality threshold
Notes: First we show how the user can tune the loss in output quality to meet desirable resiliency coverage and cost. The resiliency protection scheme we use is instruction duplication and the cost incurred is the execution overhead of the additional redundant instructions.
Using the quality profile, Approxilyzer chooses to selectively protect only those instructions that contains error sites whose output quality is neither acceptable to the user nor can be protected by low cost detectors. By not protecting the others, which we would have had to without Approxilyzer, we save on protection overhead.

## Slide 20: Approxilyzer: Ultra-Low Cost Resiliency (Water)
Chart: % Resiliency Coverage
Chart: % Resiliency Coverage
Significant resiliency overhead savings for small loss of quality
Notes: For e.g, let us consider the parsec benchmark water. The graph show
For example, for the benchmark Water,The graph here shows the coverage vs overhead curve that we would get from Relyzer, without any quality information. The x axis is Resiliency coverage- the 99% coverage point means that we protect instructions that cause 99% of the SDCs in the program, and y axis is the overhead for this coverage.
With Approxilyzer, if the user is willing to tolerate just a 1% loss in quality, we can save 55% overhead while still maintaining the high 99% coverage. And in the paer we show that for most of the applications we study, we can get significant overhead savings for very small losses in quality.

## Slide 21: Approxilyzer: First Order Approximation Potential
Identify potentially approximable instructions in the program
Eliminates instructions that produce unacceptable quality outputs
  With single bit errors unlikely to withstand more rigorous perturbations
Remaining are first order candidates for approximation
  Reduce exploration space for more targeted analysis
  Best and worst case bounds (extremes of threshold) for approximation potential
SDC-Good
SDC-Bad
SDC-Maybe
Detectable Data
Corruptions (DDC)
Masked
Detected
User acceptable quality threshold
Notes: The second broad application is using Approxilyzer to identify potential approximable instructions in the program.
We do this by eliminating instructions that contain error sites producing unacceptable quality outputs. Approxilyzer reasonable assumes that if these instructions cannot tolerate isolated single bit errors, then they probably cannot withstand more rigorous perturbation introduced by other approximation techniques.
The remaining instructions are first order candidates for approximation and by identifying them we reduce the exploration space for further targetted analysis. More generally, this enables us to automatically analyze the approximation potential of any general purpose program along different bounds and granularities.

## Slide 22
Chart: % of Static Instructions
| FI | PI_FR | PI_32b | PI_16b | PI_8b | PI_1b
Swaptions | 19.78 | 44.35 | 61.3 | 69.02 | 81.3 | 91.52
LU | 10.21 | 16.6 | 22.98 | 26.81 | 32.34 | 41.28
Blackscholes | 4.34 | 15.32 | 28.61 | 28.61 | 34.39 | 43.93
FFT | 17.67 | 27.13 | 35.35 | 53.18 | 74.11 | 82.17
Water | 23.98 | 47.52 | 50.16 | 50.28 | 59.76 | 67.8
Average | 15.196 | 30.184 | 39.68 | 45.58 | 56.38 | 65.34
Exploration of application’s approximation potential along different dimensions
15%
40%
Exploring Best-Case Approximation Potential
At least one 32b register chunk
Notes: For example, this graph asks, in the best case scenario, with virtually no quality thresholds, what is the percentage of static instructions, shown in Y axis, that are approximable under different instruction and register granularities (shown in the x axis).
The first set of data points, show that on average (show in black),15% of static instructions in the application studied are fully approximable, ie errors in all registers and all dynamic instructions are ok. If we relax the constraint a little to consider cases where only parts of the instruction is approximable, we see that 40% of static instructions have at least one continuous 32 bit register chunk that could be a candidate for approximation. We can do this kind of first order exploration along different dimensions and granularities using Approxilyzer.

## Slide 23: Conclusions
Approxilyzer :
  Minimal programmer burden, general-purpose, automatic, comprehensive
  Determines output quality at fine granularities with high accuracy (95%)
Two applications
  Ultra-low cost resiliency (upto 55% savings) for small quality loss (1%)
  First order approximation potential of applications
Future directions: Other error models, input independence, data vs. instruction
Optimizer
System Optimization; e.g.,
Resiliency vs. Cost vs. Quality
Identify potentially approximable instructions
End-to-end Quality Metric
+
APPROXILYZER
+
(Optional)
Quality Threshold
Unmodified Program
Comprehensive output quality profile
Notes: In conclusion, in this work we introduces a tool called Approxilyzer that automatically generates a comprehensive output quality profile for any general-purpose program with high precision and accuracy. Furthermore, it does so while posing the absolute minimum programmer burden. We show 2 applications of Approxilyzer, one where output quality loss can be tuned to achieve ultra-low cost resiliency and second to study the first order approximation potential of applications.
Our future work includes extending approxilyzer to other error models, make it input independent and explore approximation along data vs instruction granularity.
Thank you for your attention and I’ll now take questions.

## Slide 24
BACKUP SLIDES

## Slide 25: Quality Metrics and Thresholds

## Slide 26: Error Outcome classification

## Slide 27: Error Outcome classification