## Slide 1
GangES: Gang Error Simulation for Hardware Resiliency Evaluation
Siva Hari1, Radha Venkatagiri2, Sarita Adve2, Helia Naeimi3
1NVIDIA Research, 2University of Illinois at Urbana-Champaign, 3Intel Labs

## Slide 2: Motivation
Transient (soft) errors are important
  Need in-field low-cost reliability solution
Application level solutions are low cost
Error simulations are commonly used for resiliency evaluation
Soft Error
Output
Output
Output
Output
Output
Output
Output
Output
Output
Output
Output
Goal: Reduce the number of full error simulations

## Slide 3: State-of-the-art to Reduce Number of Simulations
Relyzer reduces number of simulations [ASPLOS’12]
BUT significant number of simulations remain
  Need ~1750 CPU hours per app
Notes: Move this to the beginning of contributions?
Relyzer is not a contribution

## Slide 4: Contributions (1/2)
GangES: Gang Error Simulator to speed up full error simulations
Output
Output
Output
Output
Output
Output
Output
Output
Output
Output
Output

## Slide 5: Contributions (1/2)
Output
Output
Output
Output
Output
Output
Output
Output
Output
Output
Output
GangES: Gang Error Simulator to speed up full error simulations
  Challenges: identifying when and what to compare
  Leverage program structure
  Shorter simulations  Faster results
  57% wall-clock time savings over Relyzer for our workloads

## Slide 6: Contributions (2/2)
Do we need error simulations at all?
Alternative is using program analysis for resiliency evaluation
  Example: lifetime, fan-out
Challenge: Hard to determine their accuracy
Relyzer + GangES enables evaluating program analyses based techniques
Found little correlation  Relyzer + GangES is best alternative
Notes: Now we have fast error simulation techniques, gives us results faster -> enables us to do this study

## Slide 7: Outline
Motivation and contributions
GangES: Gang Error Simulator
  Design
  Evaluation
Evaluating program analysis based techniques
Summary and future directions
Next

## Slide 8: Error Outcomes
Output
Output
Error-free
execution
Erroneous executions
Output
Detection
X
Silent Data
Corruption (SDC)
Detection
Masked

## Slide 9: Full Error Simulations are Time Consuming
Simulating several errors to application completion can be slow
. . .
System
State
..
.
Output
System
State
Output
..
.
System
State
Output
..
.

## Slide 10: Full Error Simulations are Time Consuming
Simulating several errors to application completion can be slow
How to shorten individual simulations and reduce redundancy?
. . .
System
State
..
.
Output
System
State
Output
..
.
System
State
Output
..
.

## Slide 11: Ganging Error Simulations
Gang Error Simulations
  Compare executions to terminate early
. . .
System
State
..
Output
..
System
State
Output
..
System
State
Output

## Slide 12: Ganging Error Simulations
Gang Error Simulations
  Compare executions to terminate early
. . .
System
State
..
Output
..
System
State
Output
..
System
State
Output
Early terminations  simulation time savings
Challenges:
  When to compare?
  What state to compare?

## Slide 13: Identifying Comparison Points
a
b
c
Leverage program structure: SESE (single-entry-single-exit) regions
  All data will flow through the exit point
SESE regions
Control-flow
edges
d
e
1
2
3
4
6
5
7
8
9
10
12
11
13
14
15
16
Notes: Motivate data will flow better – good points for comparison, all errors will flow though this point

## Slide 14: Identifying State to Compare
  Comparing full memory + processor state is expensive
Memory
State
..
Output
Output
..
Proc.
State
Memory
State
Proc.
State

## Slide 15: Identifying State to Compare
Memory
State
..
Output
Output
..
Proc.
State
Memory
State
Proc.
State
Time
All registers
–
registers written to
before being read
  Comparing full memory + processor state is expensive
Touched memory state
  Collected from same point
  Stored incrementally
Live processor register state (including PC)
  Collected by looking ahead

## Slide 16: Gang Error Simulation Algorithm
SESE exit 1
SESE exit 2
SESE exit 3
Start from a checkpoint
Injection 1
Injection 2
Gang error sites to check for equivalence
Typical group size in our framework was 100-1000
State for comparison:
(live) processor registers
+
touched memory locations
All injection runs start from the beginning of a group
Start of a gang
Notes: Explain the gang

## Slide 17: Gang Error Simulation Algorithm
SESE exit 1
SESE exit 2
SESE exit 3
Start from a checkpoint
Injection 1
Injection 2
Gang error sites to check for equivalence
Start of a gang
X
X
X
X
=
=
Only one error injection needs full simulation in this example
Injection 3

## Slide 18: Methodology for GangES
Eight applications from Parsec and SPLASH2
Error model: single bit flips in integer architectural registers (one at a time) at dynamic instructions
Employed after Relyzer
Implemented in architecture simulator (Simics)

## Slide 19: Efficacy of GangES: Wall Clock Time Savings
57% of the wall clock time saved for our workloads
Chart: Running time in hours
|  | Blackscholes |  | Fluidanimate |  | Streamcluster |  | Swaptions |  | FFT |  | LU |  | Ocean |  | Water |  | Average |  |  |  |  |  |  |  |  |  |
Baseline | 1808.4255 | 0 | 1239.0357 | 0 | 471.1342 | 0 | 1653.3533 | 0 | 2853.4341 | 0 | 447.32 | 0 | 4799.7656 | 0 | 953.8223 | 0 | 1778.2863
GangES Overhead | 0 | 14.3664 | 0 | 8.2285 | 0 | 5.0746 | 0 | 26.5417 | 0 | 8.58 | 0 | 2.5892 | 0 | 144.9858 | 0 | 14.747 | 28.1391
Need Full | 0 | 254.9651 | 0 | 328.617 | 0 | 193.4173 | 0 | 467.4084 | 0 | 1144.5465 | 0 | 128.1576 | 0 | 3020.6265 | 0 | 247.4606 | 723.1499

## Slide 20: Savings from Equalized Simulations
92% of equalized simulations require 3,025 instructions to be executed
Chart: Average instructions from error injection to successful comparison (only for saved simulations)
| Average
1 | 3024.5755
2 | 15987.4831
3 | 16848.2947
Chart: Fraction of simulations equalized at Nth SESE exit
| Average
1 | 0.9187
2 | 0.073431
3 | 0.0078657

## Slide 21: Outline
Motivation and contributions
GangES: Gang Error Simulator
  Design
  Evaluation
Evaluating program analysis based techniques
Summary and future directions
Next

## Slide 22: Evaluating Program Analysis Based Techniques
Relyzer + GangES still requires non-negligible time
  Are there faster alternatives?
Program analysis based techniques for error vulnerability
  Lifetime (average, aggregate) per instruction
  Fanout (average, aggregate) per instruction
  Dynamic instruction count
Are these effective in finding SDCs?
 Relyzer + GangES enables this evaluation
Wi
Wi
Ri
Ri
Lifetime
Notes: Higher the metric value the more vulnerable the instruction is

## Slide 23: Evaluation Methodology
Low correlation,
No common model is
effective for our apps
Five applications from Parsec and SPLASH2
Error model: single bit flips in destination integer architectural registers
Collected metric information using architectural simulator (Simics)
Employed Relyzer + GangES as golden model
Direct correlation of metrics with Relyzer +GangES
Combination of metrics
  Linear
  Linear combination on polynomials
Compare effectiveness of detectors added by Relyzer+GangES vs. simpler metrics

## Slide 24: Results: Simple Metrics are Non-trivial
Comparing the effectiveness of adding duplication based detectors
Unable to adequately predict an instruction’s vulnerability to SDCs
   Relyzer + GangES is much needed
Relyzer + GangES
Coverage of
detectors selected
using metric
Water: Fanout (agg) (Corr. Coeff. = 0.4)
Significant difference

## Slide 25: Summary and Future Directions
GangES: Effective in reducing error simulation time
  57% average wall clock time savings over Relyzer for our workloads
  Only 36% of input error sites need full application simulation
Evaluated several program analyses based techniques
  Unable to adequately predict an instruction’s vulnerability to SDCs
   Relyzer + GangES is much needed
Future direction:
  More (multi-threaded) applications, error models
  Approaches to compact the state collected for comparison
  Other program analyses based techniques

## Slide 26
Thank You

## Slide 27: Backup

## Slide 28: Relyzer vs. GangES
Relyzer is practical with 72 hrs of running time for 8 applications
90% of time is spent in error injections
Relyzer
.
.
.
Error sites in different dynamic instances of one static instruction
Error sites from pruned
instances of an instruction
.
.
GangES
.
.
Error sites in different instructions in a block
Error sites that need full application execution
Reducing full
app executions
Notes: This seems unnecessary

## Slide 29: SWAT: A Low-Cost Reliability Solution
Need handle only hardware errors that propagate to software
Error-free case remains common, must be optimized
 Watch for software anomalies (symptoms)
    Zero to low overhead “always-on” monitors
Effective on SPEC, Server, and Media workloads
<0.6% µarch errors escape detectors & corrupt application output (SDC)
Fatal Traps
Division by zero,
RED state, etc.
Kernel Panic
OS enters panic
state due to error
Hangs
Simple HW hang
detector
App Abort
App abort due
to error
Out of Bounds
Flag illegal addresses

## Slide 30: Significance of Comparing Live Processor State
21% more wall clock time savings
Chart: Running time in hours
| Blackscholes with live | without live | Fluidanimate with live | without live | Streamcluster with live | without live | Swaptions with live | without live | FFT with live | without live | LU with live | without live | Ocean with live | without live | Water with live | without live | Average with live | without live |  |  |  |  |  |  |  |  |
GangES Overhead | 14.3664 | 14.7969 | 8.2285 | 6.3823 | 5.0746 | 4.5523 | 26.5417 | 17.2652 | 8.58 | 8.5513 | 2.5892 | 2.2891 | 144.9858 | 119.5628 | 14.747 | 12.3899 | 28.1391 | 23.2237
Need Full | 254.9651 | 783.8883 | 328.617 | 358.9575 | 193.4173 | 298.2419 | 467.4084 | 536.992 | 1144.5465 | 1392.0075 | 128.1576 | 138.8634 | 3020.6265 | 3599.7372 | 247.4606 | 295.6134 | 723.1499 | 925.5377

## Slide 31: Efficacy of GangES:
Only 36% of error sites need full simulations
Chart: Fraction of error simulations
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | Average
Detected | 86741 | 21949 | 12165 | 76267 | 14375 | 9092 | 68407 | 40481 | 41184.625
Need Full | 27434 | 23710 | 21762 | 65570 | 31093 | 10638 | 259526 | 29931 | 58708
Saved | 135223 | 37312 | 19968 | 87020 | 54935 | 9605 | 112241 | 54203 | 63813.375
36%
39%
25%

## Slide 32: Why remaining?
Chart: 
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | Average
Reg Only | 14932 | 8943 | 9624 | 13586 | 9577 | 1978 | 24669 | 12339 | 11956
Mem Only | 504 | 172 | 602 | 5165 | 3196 | 327 | 36980 | 1777 | 6090.375
Reg+Mem | 7778 | 6416 | 1164 | 24853 | 7274 | 4318 | 77102 | 11320 | 17528.125
Timeouts | 4220 | 8179 | 10372 | 21966 | 11046 | 4015 | 120775 | 4495 | 23133.5

## Slide 33: Relyzer: Application Reliability Analyzer
APPLICATION
.
.
.
Output
Prune error sites
Application-level error equivalence
Predict error outcomes
Injections for remaining sites
Equivalence Classes
Pilots
Relyzer
APPLICATION
.
.
Output
Can find SDCs from virtually all application sites

## Slide 34: Pruning Results
99.78% of error sites are pruned
3 to 6 orders of magnitude pruning for most applications
  For mcf, two store instructions observed low pruning (of 20%)
Overall 0.004% error sites represent 99% of total error sites
Chart: % of all error sites
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | GCC | Libquantum | Mcf | Omnet++ | Total | Parsec 2.1 | Splash 2 | SPEC 2006 |
Remaining | 0.99996 | 0.9991 | 0.99992 | 0.99999 | 0.99999 | 0.99997 | 0.99987 | 0.99994 | 0.99875 | 0.99985 | 0.99427 | 0.99998 | 0.99781

## Slide 35: Approach: Fast Simulation Framework
Leverage program structure: SESE (single-entry-single-exit) regions*
  All data will flow through the exit point
  Check for corruption in limited state (live registers + touched memory)
SESE regions
Control-flow edges
1
2
3
4
6
5
7
8
9
10
12
11
13
14
15
16
e
d
b
a
c
*R. Johnson et al. The program structure tree: computing control regions in linear time. SIGPLAN Not., 1994
SESE Region
Other instructions
Program Structure Tree (PST)
a
b
d
c
6
3
5
e
9
1
2
4
16
8
7
11
15
10
12
14
..

## Slide 36: Results: Simple Metrics are Non-trivial
Lifetime (agg) | Fanout (agg) | Lifetime (av) | Fanout (av) | Dyn. Inst.
Poor (< 0.26) | Poor-Fair (0.21 – 0.56) | Poor (< 0.06) | Poor (< 0.05) | Poor-Good (0.27 – 0.82)
Low correlation between metrics and Relyzer for studied metrics except dyn. Inst
Notes: This graph is stale – need to update it

## Slide 37: Application Resiliency Evaluation Alternatives
Approach | Accuracy | Speed | Application coverage
Error injection | High | Low | Low
Program analysis | Hard to determine | High | High
Hybrid injection + analysis | High | Moderate | High
Our focus

## Slide 38: Results: Simple Metrics are Non-trivial
Comparing the effectiveness of adding duplication based detectors
Unable to adequately predict an instruction’s vulnerability to SDCs
   Relyzer + GangES is much needed
Relyzer + GangES
Predicted coverage of detectors selected using metric
Actual coverage of
detectors selected
using metric
Water: Fanout (agg) (Corr. Coeff. = 0.4)
Significant difference
Notes: Read the paper again